## Slide 1
Supported by
Office of
Science
NSTX
S.M. Kaye
for PPPL, U. Wisc., JHU, UCLA, UC Davis Groups
NSTX-C-Mod Pedestal Workshop
PPPL
7 Sept. 2010
NSTX Capabilities
- Turbulence and Profile Diagnostics at the Plasma Edge -
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
College W&M
Colorado Sch Mines
Columbia U
Comp-X
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Maryland
U Rochester
U Washington
U Wisconsin

## Slide 2: Multiple Diagnostics are Available to Explore Turbulence At or Near the Plasma Edge
Microwave Scattering (high-kr turbulence: ETG, TEM, mtearing): PPPL, UC Davis
Beam Emission Spectroscopy (low-k turbulence, ZFs/GAMs, AEs): U. Wisconsin
Edge Reflectometry and Backscattering (low-k, high-k, radial correlation lengths): UCLA
Interferometery (ne fluctuations <100 kHz): UC Davis
Multi-energy Soft X-ray Arrays (MHD scales,..): JHU

## Slide 3: High-k Scattering is Capable of Measuring Localized Electron Gyro-Scale Turbulence
Probe beam
280 GHz microwave is launched as the probe beam.
Coherent scattering by plasma density fluctuations occurs when the three-wave coupling condition is satisfied:
Since , ks >> , Bragg condition determines kp:
kp=2kisin(θs/2)
The scattered light has a frequency of:
ωs=ωp+ωi
with ωs and ωi >> ωp
The scattering system characteristics are:
  Frequency bandwith: 5 MHz
  Heterodyne receiver: Wave propagation direction resolved
  Measurement: kr spectrum
  Wavenumber resolution: 0.7 cm-1 (2/a with a ≈ 3 cm)
  Wavenumber range (kr): 5-20 cm-1 (~5-20 )
  Radial resolution: 2.5 cm
  Tangential resolution: 5-15 cm
  Radial range: R=106 – 144 cm
  Minimal detectable density fluctuation:
Scattered light
Spherical mirror
kp
ks
ki
2a
Probe beam
ki
ks
kp
=
+
θs
ki
kp
Y. Ren, E. Mazzucato, D. Smith,
N. Luhmann, C. Domier

## Slide 4: Electron Gyro-Scale Fluctuations are Measured in the Pedestal Region
The frequency spectra shown were measured at the pedestal region of a NB-heated H-mode plasma.
The radial resolution of 2.5 cm allows localized measurements, ideal for comparisons with turbulence theory and numerical codes.
r/a ≈ 0.87 , R ≈ 140 cm
kr ρs≈ -16.2
kθ ρs ≈ 2.84
kφ ≈ 2.53 cm-1
kr ρs ≈ -14.1
kθ ρs ≈ 2.4
kφ ≈ 2.0 cm-1
kr ρs ≈ -11.9
kθ ρs ≈ 2.0
kφ ≈ 1.6 cm-1
kr ρs ≈ -9.5
kθ ρs ≈ 1.7
kφ ≈ 1.2 cm-1
kr ρs ≈ -7.3
kθ ρs ≈ 1.0
kφ ≈ 1.0 cm-1

## Slide 5: Diagnostic Can Yield k-Spectrum of Turbulence
Scattering location
The kr spectrum does not show monotonically
increasing fluctuation power towards lower k;
measurements will be compared with results
from non-linear gyro-kinetic simulations.

## Slide 6: BES Measures Neutral Beam Da to Study Long Wavelength (krri) Density Fluctuations
Doppler shift isolates NB Dα emission from thermal Dα
Optical views are field-aligned with spatial resolution Δx ≈ 2-3 cm
RSI paper in press (Oct 2010)
Collection optics
R140
R130
D. Smith, G. McKee, R. Fonck, B. Stratton

## Slide 7: Fluctuation Amplitudes Increase During ELM Activity

## Slide 8: UCLA Reflectometers on NSTX
Millimeter-wave reflectometers available for 2010 (mid-plane)
  Ultra-fast swept FMCW reflectometers coupled with new analysis techniques
    Electron density profiles with ≥4 ms time resolution, 13-53 GHz
    Sub-millisecond turbulence radial correlations
    kr back-scattering with radial resolution
  Poloidal correlation reflectometer (2 channel, 28.5-40 GHz)
    Turbulence flow
    Poloidal correlations
    kr back-scattering with radial resolution
  16 channel fixed-frequency reflectometers (30 to 75 GHz)
    Detailed profile of coherent and turbulent fluctuation levels (2.5 MHz bandwidth)
Fixed
Frequency
Swept FMCW
Poloidal
Correlation
S. Kubota, T. Peebles

## Slide 9: Change of Turbulence at Edge Can Be Measured Through L-H Transition
kr vs R spectrogram of backscattered signal across L-H transition
  Dip in the backscattered power around the ETB location (R=146 cm) first appears near the L-H transition (~0.245 s)
  Continues to deepen during H-mode
  Consistent with picture of turbulence suppression over a wide range of kr at the ETB location

## Slide 10: Far-Infra Red Tangential Interferometer Polarimeter
FIReTIP measures line integrated
electron density including
density fluctuations ( )
2009: upgrade electronics
to yield bandwidth of 4 MHz
K.C. Lee, N. Luhmann, C. Domier

## Slide 11: Measured Growth Rates of High-k Modes Agrees with Linear GYRO Results for Fastest Growing Mode
Ch5
Ch7
Ch3
0.22
20-
40-
60-
80-
0.23
0.24
0.22
0.23
0.24
0.22
0.23
0.24
L
H
Example of turbulence suppression
Edge channels (Ch5: RT=132 cm,
Ch7: RT=150 cm) showed clear decrease
Fluctuations decrease in frequency range
of < 100 kHz
f(kHz)

## Slide 12: Profile Diagnostics
Thomson Scattering
  30 channels presently, 40 after upgrade
    6-9 mm spatial resolution in outer region
    2 lasers with flexible timing (generally one profile measurement every 16 ms)
CHERS
  51 spatial channels
    Down to 1-2 cm spatial resolution (~1 ri in outer region)
    10 ms temporal resolution

## Slide 13: Multi-Energy SXT Designed for High Spatial Resolution (< 1 cm) of Outer Plasma (r/a>0.5)
K. Tritz, D. Stutman, M. Finkenthal, D. Kumar, D. Slayton