## Slide 1
“Snowflake” divertor configuration in NSTX*
V. A. Soukhanovskii (LLNL)
D. D. Ryutov, H. A. Scott (LLNL), R. Maqueda (Nova Photonics),
J.-W. Ahn, R. Maingi, A. McLean (ORNL),
R. Bell, D. A. Gates, S. Gerhardt, R. Kaita, E. Kolemen, B. P. LeBlanc, J. E. Menard, D. Mueller, S. F. Paul, A. L. Roquemore (PPPL),
R. Raman (U Washington)
Poster P 2.161
22 June 2010
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
* Supported by the U.S. DOE under Contracts DE-AC52-07NA27344, DE AC02-09CH11466, DE-AC05-00OR22725, DE-FG02-08ER54989.

## Slide 2: Abstract
The studies of an innovative "snowflake" divertor (SFD) configuration in the National Spherical Torus Experiment (NSTX) provide support to this plasma-material interface concept as a promising candidate for future tokamaks and spherical tokamak based devices with high heat flux divertors. A number of theoretically predicted geometric and radiative properties of the SFD configuration [1-4] have been confirmed in experiments at NSTX. The obtained SFD showed evidence of impurity control and divertor heat flux reduction. The SFD configuration was obtained in 1 MA 4-6 MW NBI-heated H-mode discharges with PSOL ~ 3 MW. Two divertor coils with 4 and 12 kA current waveforms controlled by the plasma control system were used to generate the SFD. A very high poloidal flux (area) expansion of the separatrix region in the SFD, a longer connection length and a larger divertor scrape-off layer (SOL) volume (as compared to standard NSTX divertor configurations) led to a partial detachment of the first several mm of the SOL width (as mapped to the midplane). Divertor heat flux profiles showed a significant reduction of the peak values, accompanied by an increase in divertor radiated power. A volume recombination zone with Te ~ 1.5 eV, ne ~ 2-6 x 1020 m-3 developed in the X-point and strike point regions, suggesting an increase in volumetric momentum losses in the divertor. The core carbon density was reduced by up to 50 % in the SFD discharges with no degradation of H-mode stored energy and confinement.
[1] D. D. Ryutov, Phys. Plasmas 14, 64502 (2007)
[2] D. D. Ryutov et. al., Phys. Plasmas 15, 092501 (2008)
[3] D. D. Ryutov et al., Paper IC/P4-8, 22st IAEA FEC, Geneva, Switzerland, 10/2008
[4] M. V. Umansky et al., Nucl. Fusion 49, 075005 (2009)

## Slide 3: Overview and Summary
“Snowflake” divertor configuration – a promising solution for divertor heat flux mitigation in future fusion plasma devices
“Snowflake” divertor configuration (cf. standard divertor)
  Higher flux expansion (increased divertor Awet )
  Higher divertor volume (increased Prad, Rrec, Rcx)
  Existing divertor magnetic coils for control
In recent NSTX experiments
  “snowflake” divertor was generated with 2 divertor coils
  H-mode confinement maintained
  “snowflake” divertor led to outer strike point partial detachment
    significant reduction in peak heat flux
    reduction of core impurities
  predicted “snowflake” divertor geometry properties confirmed

## Slide 4: Various techniques considered for SOL / divertor q|| and qpk control
Divertor heat flux mitigation solutions:
  Divertor geometry (poloidal flux expansion)
  Strike point sweeping
  Radiative divertor (or radiative mantle)
  Divertor plate tilt and divertor magnetic balance
Candidate solutions
  be compatible with good core plasma performance (H-mode confinement, MHD, ELM regime, density) and particle control
  scale to very high qpeak (15 - 80 MW/m2) for future devices

## Slide 5: Open divertor geometry and extensive divertor diagnostics enable divertor configuration studies in NSTX
Plasma facing components
  ATJ and CFC graphite tiles
  Lithium coatings from overhead lithium evaporators

## Slide 6: Theory predicts attractive divertor geometry properties in “snowflake” divertor configuration
Proposed by D. D. Ryutov (LLNL)
  Phys. Plasmas 14, 064502 (2007)
  34th EPS Conference on Plasma Phys. Warsaw, 2 - 6 July 2007 ECA Vol.31F, D-1.002 (2007)
  Phys. Plasmas, 15, 092501 (2008)
  Paper IC/P4-8 at IAEA FEC 2008
SFD is obtained by creating a second-order poloidal null in the (lower) divertor with existing divertor coils
Predicted properties (cf. standard divertor)
  Lower Bp in X-point region
  Larger Awet , fexp
  Larger X-point connection length Lx
  Larger effective divertor volume Vdiv
  X-point flux tube squeezing – barrier for turbulence?
  ELM control (increased edge magn. shear) ?
Ideal
“snowflake”
divertor
“snowflake”-plus “snowflake”-minus
divertor configurations

## Slide 7: ISOLVER code was used to obtain strike point positions and divertor coil currents of “snowflake” configuration
Modeled “snowflake” divertor configurations
ISOLVER - predictive free-boundary axisymmetric equilibrium solver was used to model divertor coil currents for NSTX “snowflake” configurations
Standard divertor configuration “Snowflake” divertor configurations obtained in NSTX
+
+
Null-point separation d

## Slide 8: In experiment, “snowflake” divertor configuration was obtained via controlled outer strike point scan
Scanned OSP between 0.44 to 0.73 m on a shot-to-shot basis
Best “snowflake” configurations were obtained with requested ROSP ~ 0.55 m (not necessarily actual ROSP)
“Snowflake” configuration was obtained when null-point separation d decreased to below 20 cm

## Slide 9: Theoretically predicted geometrical properties of the snowflake divertor configuration are confirmed in NSTX
In “snowflake” divertor
  Plasma-wetted area (flux expansion) higher by up to 50 %
  Lx longer (thus fPFR and Vdiv higher)
These properties observed in first 2-3 mm of SOL lq

## Slide 10: H-mode confinement retained with “snowflake” divertor, core Prad and nC reduced by up to 75 %
Used 80-100 g evaporated lithium per discharge for wall conditioning
ELM-free H-mode discharges had impurity accumulation
In “snowflake” divertor discharges
  Divertor sputtering source reduction (?)
  Edge confinement degradation (?)

## Slide 11: Partial detachment of outer strike point region observed in “snowflake” divertor discharges
Signs of partial detachment observed in “snowflake” divertor
  Loss of parallel pressure
  Heat and particle flux reduction at the plate
  Te ≤ 1.6 eV, ne ≥ 2e14 m-3
  Increase in divertor Prad
  Increase in 3-body recombination rate
  Increase in neutral pressure

## Slide 12: Significant reduction of heat flux observed in “snowflake” divertor
Divertor peak heat flux well correlated with null-point separation d
Reduction observed in 2-3 mm region (mapped to midplane) adjacent to separatrix
Shown heat fluxes are in uncalibrated relative units (IR camera data not calibrated due to lithium coatings)

## Slide 13: Divertor particle flux decreased, Balmer-a intensity increased (due to recombination) in “snowflake” divertor
Divertor Da emission
  Increase in radiating zone width
  Brightness increase (due to recombination) correlated with Langmuir probe Isat decrease (due to particle flux reduction)

## Slide 14: High-n Balmer line emission measurements suggest high divertor recombination rate, low Te, high ne
Te=0.8-1.2 eV, ne=2-7 x 1020 m-3 inferred from modeling
Balmer series spectra modeled with CRETIN; Spectra sensitive to
  Line intensity <-> Recombination rate
  Te <-> Boltzman population distribution
  ne <-> Line broadening due to linear Stark effect from ion and electron microfield
“snowflake”
standard

## Slide 15: Divertor camera images show formation of extended radiation zone in “snowflake” divertor
Visible camera images (~ 400 – 750 nm bandpass)
Larger radiative zone in “snowflake” divertor (cf. standard divertor)
Center stack
gas puff

## Slide 16: Volumetric power and momentum losses are increased due to geometry in “snowflake” divertor
Hulse-Post non-coronal radiative cooling curves for low Z impurities for n0/ne, ne-recy
Calculate max q|| that can be radiated
Express max q|| as function of distance from heat source for range of fz (Post JNM 220-222, 1014 (1995) )
Power losses due to deuterium Prad and ionization not considered
For NSTX, use n0 = 0.1 % and ne-recy = ne x 1e-3 s
Electron-ion recombination rate depends on divertor ion residence time
  Ion recombination time: ion~ 1−10 ms at Te =1.3 eV
  Ion residence time:ion  3-6 ms

## Slide 17: Future plans
Magnetic control of “snowflake” divertor
  RT-control of 2nd null-point with PCS
  Use of PF1B for control
Transport and turbulence characterization
Edge stability characterization
Scaling with power
High-performance plasma scenario with lithium
conditioning and reduced core impurities
NSTX-Upgrade (Poster P2.106 by J. E. Menard)
  Additional divertor coil PF1C
    flux expansion variation with fixed X-point height
    and strike-point location
  Development of PMI solutions to address
    2-3x higher input power
    up to 30 % reduction in Greenwald fraction
    3-5 x longer pulse duration