## Slide 1: Disruption event characterization and forecasting of global and tearing mode stability for tokamaks
J.W. Berkery, S.A. Sabbagh, and J.D. Riquezes
Columbia University
S.P. Gerhardt and C.E. Myers
Princeton Plasma Physics Laboratory
2nd IAEA Technical Meeting on Fusion Data Processing, Validation and Analysis
Boston, MA
May 30- June 2, 2017
*This work is supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: Outline
The Disruption Event Characterization And Forecasting (DECAF) code
  Contains various physical event modules with warning algorithms
A reduced kinetic model for resistive wall mode stability
  Complex calculation reduced for speed, performs well
Identification of rotating MHD
  Tracks characteristics that lead to disruption: rotation bifurcation, mode lock

## Slide 3: Disruption event chain characterization capability started as next step in disruption avoidance plan
t
[DOE report on Transient events (2015)]
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
  Cues disruption avoidance systems to break event chains
    Attack events at several places with active control
  Builds upon both physics and control successes of NSTX

## Slide 4: Disruption Event Characterization And Forecasting (DECAF) code is structured to ease parallel development
Main data structure
Code control workbooks
Density Limits
Confinement
Technical issues
Tokamak dynamics
Power/current handling
Mode stability
Physical event modules
Output processing
RWM and tearing mode stability
Physical event modules
  Present grouping follows work of deVries [P.C. de Vries et al., Nucl. Fusion 51, 053018 (2011)]
  – BUT, easily appended or altered
Warning algorithms
  Present approach follows [S.P. Gerhardt et al., Nucl. Fusion 53, 063021 (2013)]
  More flexible: arbitrary number of tests, thresholds, and user-defined levels and warning points

## Slide 5: Several threshold tests are currently included in DECAF

## Slide 6: Example DECAF analysis on single NSTX discharge
NSTX
NSTX 140132
DECAF uses simple threshold tests and more sophisticated models to declare events
  Ex: RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)

## Slide 7: Example DECAF analysis on single NSTX discharge
DECAF uses simple threshold tests and more sophisticated models to declare events
  Ex: RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
Tests can be combined with “warning points”
  Ex: VSC uses Z, dZ/dt, and ZdZ/dt

## Slide 8: Initial DECAF results detects disruption chain events when applied to dedicated 45 shot NSTX RWM disruption database
RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
60% within 14 τw of disruption time (τw = 5 ms)
unstable RWM
137722
140102
NSTX
RWM events in DECAF
Disruption
  IPR: Plasma current request not met
  RWM: RWM event warning
  VSC: Vertical stability control
  LOQ: Low edge q warning

## Slide 9: Initial DECAF analysis already finding common disruption event chains, giving new insight
Identifying common chains of events can provide insight to cue avoidance systems
  5 (out of theoretically 56) two-event combinations followed 77% of RWM cases (those that occurred within 14τw of DIS)
Earlier RWM events not false positives
  cause large decreases in βN and stored energy with subsequent recovery (minor disruptions)
VSC
VSC
WPC
PRP
IPR
Other
RWM
PRP
WPC
VSC
VSC
WPC
30.8%
19.2%
11.5%
7.7%
7.7%
23.1%

## Slide 10: Outline
The Disruption Event Characterization And Forecasting (DECAF) code
  Contains various physical event modules with warning algorithms
A reduced kinetic model for resistive wall mode stability
  Complex calculation reduced for speed, performs well
Identification of rotating MHD
  Tracks characteristics that lead to disruption: rotation bifurcation, mode lock

## Slide 11: Goal is to forecast mode growth rate in real-time using parameterized reduced models for δW terms
no-wall limit
no-wall limit
with-wall limit
with-wall limit
fluid RWM growth rate
stabilized by kinetic effects
β limits
δW
growth
rate
(γτw)
RWM dispersion relation
Gaussian functions used for resonances
  Coefficients selected to reflect NSTX experience
Kinetic effects:
Fluid terms
Rotation
Collisionality
Bounce resonances
Precession resonance
<ν> = 1 kHz

## Slide 12: DECAF contains modeled kinetic quantities for generation of stability maps
Normalized growth rate vs. time
Stability diagram shows trajectory of a discharge towards unstable regions
Fluid
Fluid + Kinetic
unstable
stable
unstable
region
Cβ
Cβ =
(βN – βNno-wall)/
(βNwith-wall – βNno-wall)

## Slide 13
Normalized growth rate vs. time
unstable
stable
(7%) False
positives
DECAF reduced kinetic model results initially tested on a database of NSTX discharges with unstable RWMs
unstable
stable
Predicted instability statistics (45 shots)
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
(7%) False
positives
44% predicted unstable < 320 ms (approx. 60τw) before current quench
33% predicted unstable within 100 ms of a minor disruption

## Slide 14: Reduced kinetic model distinguishes between stable and unstable NSTX discharges
If <ωE> ~ 0 warnings are eliminated, 10/13, or 77%, of stable cases are stable in the model
Model is successful in first incarnation - development continues to improve forecasting performance
Tradeoff: missed vs. early warnings
Unstable cases
Stable cases

## Slide 15: Outline
The Disruption Event Characterization And Forecasting (DECAF) code
  Contains various physical event modules with warning algorithms
A reduced kinetic model for resistive wall mode stability
  Complex calculation reduced for speed, performs well
Identification of rotating MHD
  Tracks characteristics that lead to disruption: rotation bifurcation, mode lock

## Slide 16: Essential new step for DECAF analysis of general tokamak data: Identification of rotating MHD (e.g. NTMs)
Initial goals
  Create portable code to identify existence of rotating MHD modes
  Track characteristics that lead to disruption
    e.g. rotation bifurcation, mode lock
Approach
  Apply FFT analysis to determine mode frequency, bandwidth evolution
  Determine bifurcation and mode locking
Magnetic spectrogram of rotating MHD in NSTX
n = 1 mode frequency vs. time
ω0 ~ 9 kHz
bifurcation ~ 4 kHz
NSTX “stable periods” – enhanced by high elongation (κ ~ 2.7), lithium wall conditioning
NSTX-U: rotating MHD more common (lower κ ~ 2.3, no lithium)

## Slide 17: DECAF rotating MHD analysis identifies the state of the modes found
mode lock
B (G)
20
10
0
-10
-20
-30
B (G)
30
-30
-20
-10
20
10
0
0.68
0.70
0.72
0.74
0.76
0.78
time (s)
Fast Fourier transforms used to find mode peak frequency within a time interval
Odd-n
Even-n
FFTs
Signals
Odd-n
Even-n

## Slide 18: DECAF rotating MHD analysis identifies the state of the modes found
Frequency vs. time
1 = mode rotating
0 = No mode
DECAF mode status
t (s)
0
-1
1
-1 = mode locked
1 = mode rotating
0 = No mode
-1 = mode locked
0
-1
1
Odd-n
Even-n
0.66
0.70
0.74
0.78

## Slide 19: The characterization algorithm shows that the expected bifurcation and locking events can be found
Algorithm written looks for a “quasi-steady state” period, a potential bifurcation, and possible mode locking
NSTX-U shot 204202
odd-n peak frequencies
lock
NSTX shot 138854
odd-n peak frequencies
lock
Mode frequency
bifurcates

## Slide 20: Conclusions
The DECAF code can characterize chains of events leading to disruption
  Expanding set of modules and warnings used to analyze data sets
A reduced kinetic model for resistive wall mode stability
  Complex calculation reduced for speed, performs well
Algorithm for identifying rotating MHD can find frequency, bifurcation points, locking times

## Slide 21: Backup

## Slide 22: DECAF contains modeled quantities for stability estimation
[J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
Modeled estimates for NSTX no-wall limit
NSTX 138556
DCON
Above no-wall
limit
Below
Internal inductance
Pressure peaking
Aspect ratio
Composite no-wall limit model
DECAF
DECAF replicates published NSTX βN no-wall model
DECAF δW no-wall model similar to DCON results

## Slide 23: DCON confirms NSTX-U above the no-wall limit; NSTX-based model gives good estimate
NSTX-U H-mode discharges: 204112
204118 (April 2016)
NSTX no-wall limit model ([J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]) includes internal inductance, pressure peaking, and aspect ratio, predicts NSTX-U DCON no-wall limit
DCON
Above no-wall limit
Below
Composite no-wall limit model
DCON
Above no-wall limit
Below
Composite no-wall limit model