## Slide 1
Diagnostic options for radiative divertor feedback control on NSTX-Upgrade
V. A. Soukhanovskii
S. P. Gerhardt, R. Kaita, A. G. McLean, R. Raman
and the NSTX Research Team
Poster P.6.18
19th Topical Conference High-Temperature Plasma Diagnostics Monterey, CA, May 6-10, 2012
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Outline - Developing real-time radiative divertor feedback control for NSTX-U
Impurity-seeded radiative divertor technique is one of the leading candidates to mitigate divertor heat flux in NSTX-U discharges
  Unmitigated 20-30 MW/m2 peak heat fluxes predicted
Radiative divertor feedback control being developed for NSTX-U
  Proportional, integral, derivative process controller to be used in digital plasma control system
  Fast piezoelectric valve is the actuator
    Gas flow rate is proportional to control voltage
  Control signal diagnostics for divertor detachment identification and control (System ID) are discussed in this poster
    Divertor ID diagnostics
      IR thermography
      Thermoelectric current
      Impurity VUV spectroscopy and bolometry
      Neutral gas pressure
      Electron-ion recombination rate via UV/NIR spectroscopy
    Pedestal ID diagnostics

## Slide 3: Abstract
A radiative divertor technique is used by present day tokamak experiments and planned for ITER to mitigate high heat loads on divertor plasma-facing components to prevent their excessive erosion and thermal damage. The radiative divertor uses induced plasma volumetric power and momentum losses to reduce heat and particle flux density on divertor target plates. Extrinsically seeded deuterium or impurity gases have been employed to control divertor parameters in several tokamak experiments via a real-time feedback control of the gas seeding rate, providing design guidelines for the radiative divertor control system in ITER [1].
In the National Spherical Torus Experiment (NSTX), a medium-size spherical tokamak with lithium-coated graphite plasma-facing components (PFC) and high divertor heat flux (qpeak ≤ 15 MW/m2, q|| ≤ 200 MW/m2 [2]), radiative divertor experiments employed deuterium, methane, and neon preprogrammed gas injections. A significant reduction of divertor peak heat flux simultaneously with good core H-mode confinement has been demonstrated [3]. In the NSTX-U device, steady-state peak divertor heat fluxes are projected to 20-30 MW/m2 [2]. In this work we use NSTX radiative divertor results to analyze diagnostic options applicable to NSTX-U for real-time feedback control of divertor heat flux.
The divertor detachment process is device-specific w.r.t. seeding gas species, radiating impurity, and onset parameters, albeit universally measured signatures such as reduction of divertor qpeak, increase in divertor ne and decrease in Te to below 2-3 eV, increase in Prad, reduction of particle flux density and increase in recombination rate. Characteristic detachment onset time and spatial extent define diagnostic requirements to the control signal: the time resolution 5-10 ms and the spatial resolution of 1 cm. Two-dimensional coverage might be desirable. Based on the NSTX divertor detachment signatures [3], we identify three categories of diagnostics that can be used for control signals: 1) PFC diagnostics (e.g., surface temperature, impurity influx measurements); 2) divertor plasma diagnostics (e.g., radiated power, impurity spectroscopy, neutral or impurity gas pressure, ion flux, divertor Te and ne, ion recombination measurements); 3) scrape-off layer and pedestal diagnostics (e.g., monitoring MARFEs or pedestal degradation signs). These radiative divertor signatures are analyzed for uniqueness and ranked in utility. Once the control signal is unambiguously linked to the radiative divertor state identification, it can be fed into a real-time plasma control system that uses an algorithm (e.g., the proportional-integral-derivative controller) to compare the control signal to the set value, quantify the difference, and feedback on the control signal using impurity seeding as an actuator.
[1] ITER Physics Expert Group on Divertor, Nucl. Fusion 39 (1999 ) 2391; Nucl. Fusion 47 (2007) 8203
[2] T. K. Gray et al., J. Nucl. Mater. 415 (2011) S360
[3] V. A. Soukhanovskii et al., Phys. Plasmas 16 (2009) 022501; Nucl. Fusion 49 (2009) 095025

## Slide 4: Divertor heat flux mitigation is key for present and future fusion plasma devices
Radiative divertor is envisioned for
present and future devices (e.g. ITER, ST-FNSF) as the steady-state heat flux mitigation solution
  Divertor qpeak < 10 MW/m2
  Large divertor radiated power fractions
  (frad = 0.50 - 0.80)
  Integration with pedestal and core
  Partial divertor strike point detachment is the
  most promising regime
Peng et al, PPCF 47, B263 (2005)

## Slide 5: Multiple diagnostic measurements were needed to elucidate on radiative divertor physics in NSTX
Plasma facing components
  ATJ and CFC tiles, lithium coatings
  Max Prad fraction limited by impurity radiation efficiency (Li, C)
  Typical divertor tile temperature in 1 s pulses T < 500 C (qpeak  10 MW/m2)

## Slide 6: Models used to simulate detachment operation space and divertor plasma parameters during detachment
Operating space Pin, ne
UEDGE calculations predicted limited “window” of outer divertor strike point detachment
Radiation from intrinsic carbon at 3-5 %
G. Porter
N. Wolf
5-zone 1D SOL model predicts typical Te and ne in NSTX during detachment
High frad ~0.8-0.9 used for detachment simulation
SOUKHANOVSKII, V. et al., Phys. Plasmas 16 (2009) 022501,
SOUKHANOVSKII, V. et al., J. Nucl. Mater. 363-365 (2007) 432.

## Slide 7: Radiative divertor experiments using low   configuration showed qpeak reduced albeit with confinement degradation
Peak heat flux in outer divertor:
  ITER-level qout< 10-15 MW/m2
  Scaling of qpeak: linear with Psol (PNBI), linear-monotonic with Ip
  Large qpeak asymmetry - 2-10; inner divertor always detached
Experiments using D2 injection:
  qpeak reduced by up to 60 % in transient detachment regime
  X-point MARFE degraded confinement within 2-3 x E
GRAY, T. et al., J. Nucl. Mater. 415 (2011) S360,
SOUKHANOVSKII, V. et al., IAEA FEC 2006

## Slide 8: Good core plasma performance and significant qpeak reduction obtained in high  detached divertor
Experiments conducted in 0.8-1.2 MA 4-6 MW NBI-heated H-mode discharges with k=2.2-2.3, d=0.6-0.75
Obtained partially detached divertor outer strike point using divertor D2 injection; Prad due to intrinsic carbon
qpeak reduced by 60 - 80 % with min. confinement degradation
SOUKHANOVSKII, V. et al., Phys. Plasmas 16 (2009) 022501,
SOUKHANOVSKII, V. et al., Nucl. Fusion 49 (2009) 095025

## Slide 9: NSTX Upgrade will address critical plasma confinement and sustainment questions by exploiting 2 new capabilities
TF OD = 40cm
TF OD = 20cm
Previous
center-stack
  2x higher CD efficiency from larger tangency radius RTAN
100% non-inductive CD with q(r) profile controllable by:
  NBI tangency radius
  Plasma density
  Plasma position
New 2nd NBI
Present NBI
Reduces n*  ST-FNSF values to understand ST confinement
  Expect 2x higher T by doubling BT, IP, and NBI heating power
  Provides 5x longer pulse-length
  q(r,t) profile equilibration
  Tests of NBI + BS non-inductive ramp-up and sustainment
New
center-stack
New center-stack
New 2nd NBI
MENARD, J. et al., Proceedings of the 24th IEEE Symposium on Fusion Engineering (2011).

## Slide 10: NSTX-U scenarios with high Ip and PNBI are projected to challenge passive cooling limits of graphite divertor PFCs
High IP scenarios projected to have narrow lqmid  ~3mm
  At high power, peak heat flux ≥ 9MW/m2 even with high flux expansion ~60 with U/L snowflake
  Numbers shown ignore radiation, plate tilt, strike-point sweeping
Long-pulse + high IP and power may ultimately require active divertor cooling
Passive cooling ok for low-IP scenarios
MENARD, J. et al., Proceedings of the 24th IEEE Symposium on Fusion Engineering (2011).
R. Maingi (ORNL)

## Slide 11: Radiative divertor control options are affected by NSTX-U plasma-facing component development plan
Baseline
All Mo PFCs
Mo wall
+ W divertor
All Mo tiles
All
Mo divertor
Upper
Mo divertor
Possible progressions
5 yr plan
C
BN
C
BN
Mo
C
BN
Mo
BN
Mo
Mo
Mo
W
Developing PFC plan to transition to full metal coverage for FNSF-relevant PMI development
Wall conditioning: GDC, lithium and / or boron coatings
PFC bake-out at 300-350oC
Radiative divertor elements affected by PFC choice:
  Divertor impurity gas handling and injection system
    D2, CD4, Ar with graphite PFCs and lithium coatings
    D2, N2, CD4, Ar with refractory metal PFCs
  Diagnostic sensors for control
  Plasma Control System development
Mo tiles

## Slide 12: Impurity-seeded radiative divertor with feedback and snowflake geometry are the leading NSTX-U heat flux mitigation candidates
NSTX-U scenarios with high Ip and Pin projected to challenge thermal limits of graphite divertor PFCs
Single and double-null radiative divertors and upper-lower snowflake configurations considered
  Supported by NSTX-U divertor coils and compatible with coil current limits
Snowflake divertor projections to NSTX-U optimistic
  UEDGE modeling shows radiative detachment of all snowflake cases with 3% carbon and up to PSOL~11 MW
    qpeak reduced from ~15 MW/m2 (standard) to 0.5-3 MW/m2 (snowflake)
  Snowflake divertor with impurity seeding for PSOL ~ 20 MW under study
NSTX-U
snowflake
simulation
E. Meier (LLNL)

## Slide 13: Conceptual design of radiative divertor feedback control system is based on PID control
Proportional, integral, derivative controller

## Slide 14: Control signal options demonstrated using divertor outer strike point partial detachment with D2 or CD4 puffing
4MW NBI-heated H-mode
  CD4 injection preprogrammed wave form
Outer strike point detachment occurred at about 0.7 s (red traces)
  Characteristic onset time 50 ms
Divertor detachment affected divertor power balance
  Carbon radiation and Prad increased
  Divertor heat flux decreased
Divertor detachment affected SOL momentum balance
  Neutral pressure increased (also due to gas puffing)
  Divertor volumetric recombination rate increased (Balmer line intensities increased)

## Slide 15: Option 1: IR thermography for divertor surface temperature monitoring
Diagnostic principle and description
  Measure PFC surface IR emission, calibrate for temperature
  IR arrays (1D or 2D) or single-channel IR diode with strike-point region view
Signal details from NSTX experiments
  Detached region localization: 5-12 cm
  Characteristic time: 1 ms
  X 4 reduction during detachment
Advantages:
  Direct PFC temperature monitoring
Issues:
  Toroidal and poloidal localization
  Interpretation and calibration issues due to PFC coatings (e.g., lithium)
Implementation
  Needs special IR and relay optics
  IR optics
AHN, J.-W. et al., Rev. Sci. Instrum. 81 (2010) 023501.
detachment

## Slide 16: Option 2: monitor SOL thermo-electric current representative of divertor electron temperature
Diagnostic principle and description
  SOL thermoelectric current due to divertor Te difference
  Electric current and potential
Signal details from NSTX experiments
  In NSTX inner and outer vessels electrically isolated
  Potential V measured in CHI exp’s
RAMAN, R. et al., Nucl. Fusion 49 (2009) 065006
STAEBLER, G. et al., Nucl. Fusion 29 (1989) 1820
KALLENBACH, A. et al., J. Nucl. Mater. 290-293 (2001) 639
Advantage:
  Toroidally-averaged current and potential, linked to divertor Te
Issues:
  More experiments needed to improve interpretation
Measure V, I

## Slide 17: Option 3: Monitor divertor radiated power or spectroscopic representation of radiated power
Diagnostic principle and description
  Fast bolometer or AXUV diode (or array) to monitor divertor rad. power
  VUV spectroscopy
Advantage:
  Toroidally-averaged quantity linked to seeded impurity radiation
Issues:
  Need to know radiation distribution and spectral composition
Implementation
  Existing AXUV diode array (s)
  Divertor SPRED
  Dedicated divertor VUV monitor
SOUKHANOVSKII, V. et al., Rev. Sci. Instrum. 70 (1999) 340
SOUKHANOVSKII, V. et al., Rev. Sci. Instrum. 72 (2001) 3270

## Slide 18: Option 4: Monitor neutral pressure
Diagnostic description
  Penning gauge for gas pressure monitoring in range 0.1-5 mTorr
Signal details from NSTX experiments
  Divertor pressure measured in private flux region, outer strike point region
Advantages:
  Direct seeding gas pressure measurement
Issues:
  Need to understand links to detachment characteristics
Implementation
  Straightforward, existing gauges can be used
  Developing calibrated spectroscopic monitoring of Penning gauge
FINKEN, K. et al., Rev. Sci. Instrum. 63 (1992)

## Slide 19: Option 5: Monitor recombination rate via Balmer or Paschen line spectroscopy
Diagnostic description
  UV or NIR spectroscopy to monitor emission line intensity from high-n Balmer or Paschen series lines
Signal details from NSTX expt’s
  Strong indication of detachment, signal increases by up to 102
  Observed n=2-m, m=3-12 (Balmer)
  Observed n=3-m, m=5-10 (Paschen)
Advantages:
  Toroidally-averaged quantity
  Direct measure of recombination rate
Implementation
  Can use existing UV and NIR fibers and instruments
SOUKHANOVSKII, V. et al., Rev. Sci. Instrum. 77 (2006) 10127
SOUKHANOVSKII, V., Rev. Sci. Instrum. 79 (2008) 10539
SOUKHANOVSKII, V. et al., Rev. Sci. Instrum. 81 (2010) 10723.

## Slide 20: Option 6: need “security” monitoring for signs of confinement degradation (pedestal temperature or MARFEs)
Diagnostic principle and description
  Monitor pedestal Te (100-600 eV)
    Soft X-ray arrays, real-time Thomson
  Monitor MARFE formation
    Edge neutral pressure
    Divertor recombination rate
Optimal D2 injection rate found (used 300 ms pulses)
50-100 Torr l /s for 1.0 MA discharges
110-160 Torr l /s for 1.2 MA discharges
X-point MARFE formation during high-rate supersonic gas injection. Balmer B10 line intensity is plotted.