## Slide 1: Beam emission spectroscopy measurements on NSTX: diagnostic performance and low-k turbulence characterization
David R. Smith1, R. Fonck1, G. McKee1, D. Thompson1, B. Stratton2, and I. U. Uzun-Kaymak1
1University of Wisconsin-Madison 2Princeton Plasma Physics Lab
19th High Temperature Plasma Diagnostics Conference
Monterey, CA
May 6-10, 2012

## Slide 2: What are the characteristics and parametric dependencies of pedestal turbulence in NSTX?
ITER and next-step devices need accurate models of pedestal dynamics
  Global confinement predictions
  Diverter heat flux and first-wall lifetime predictions
  ST edge parameters are among the most challenging regimes for turbulence simulations (steep gradients, high b, large ri/a, strong shaping)
Here, we measure pedestal turbulence parameters in NSTX H-mode plasmas during ELM-free, MHD quiescent periods
  Poloidal correlation length, wavenumber, and decorrelation time
  Identify parametric dependencies (∇ne, ∇Ti, etc)
NSTX: BES
measurements
from multiple discharges in steep gradient region
C-Mod: stored energy increases with pedestal height
Hughes, PoP, 2002

## Slide 3: Outline
Beam emission spectroscopy (BES) diagnostic on NSTX
Pedestal turbulence measurements
  LH transition
  ELM-free, MHD quiescent periods
  Parametric scalings
Correlation length during the ELM cycle
  Initial theory/experiment comparison
Other BES observations
  Post-ELM harmonic features
  TAE and GAE mode structures
Future work and summary

## Slide 4: Beam emission spectroscopy (BES) is a diagnostic technique for measuring ion gyroscale (kρi < 1) density fluctuations
Measured & derived quantities
  Fluctuation amplitudes
  Frequency spectra
  Radial and poloidal correlation lengths
  Decorrelation times
  Poloidal flow, flow fluctuations, flow shear, and 2D flow fields
  2D fluctuation imaging
  3-wave bispectral analysis
  Particle flux
Figures courtesy of
DIII-D BES group

## Slide 5: BES measures Doppler-shifted Da emission (l0=656 nm) from neutral beam particles
neutral beam Da emission
density
fluctuation
C ≈ 1/2

## Slide 6: MSE & FIDA measurements on NSTX indicate NB Da emission is comparable to or greater than C-II emission
MSE spectrum
tangential view with
large red-shift in NB Da
and long-time integration
FIDA spectrum
vertical view with
small blue-shift in NB Da
and short-time integration
MSE & FIDA spectra
indicate:
Also, C-II fluctuations should average out due to large C-II sampling volume.
Courtesy of H. Yuh & F. Levinton
Courtesy of M. Podesta & W. Heidbrink

## Slide 7: Optical views are aligned to the magnetic field pitch angle within the NB volume to optimize cross-field spatial resolution
Reentrant optics increase light collection

## Slide 8: The NSTX BES system has 56 sightlines in radial and poloidal arrays spanning core to SOL
32 detection channels presently and expansion planned for NSTX-U
2 MHz sampling with digital anti-alias filter
2-3 cm image size and sensitive to ñ with k┴ri ≤ 1.5
Field-aligned optics with high throughput (etendue = 2.3 mm2-ster)

## Slide 9: Point spread function calculations indicate image distortion from atomic state lifetimes and field line geometry are negligible
field line misalignment
nearly optimized
low density region
distortion from misalignment (dashed=10% of peak int.)
distortion from
atomic state lifetimes
FWHM distortions (solid line) are ~10%

## Slide 10: NSTX BES system was commissioned in 2010
Collection optics
Detector module
Photodetector
Fiber images

## Slide 11: BES measurements show radially-localized response to neutral beam emission and high signal-to-noise ratio

## Slide 12: BES measurements provide poloidal correlation lengths (Lc), poloidal wavenumbers (kq), and decorrelation times (td) in the pedestal
Filtered data shows eddy propagation
Turbulence quantities calculated from time-lag cross-correlations

## Slide 13: Edge and core regions show reduced fluctuations at LH transition
Similar increase in fluctuations observed at HL back-transitions

## Slide 14: Pedestal measurements show complex turbulence activity during quiescent H-mode periods

## Slide 15: Questions about pedestal turbulence to ask and answer with BES measurements
What are typical Lc, kq, and td values in the H-mode pedestal during ELM-free, MHD quiescent periods?
How do Lc, kq, and td change with plasma parameters?
  ∇ne, ∇Ti, q/ŝ, ne, be, nped, etc.
Can we connect observations to edge turbulence simulations?
  XGC1 or BOUT++?

## Slide 16: Pedestal turbulence measurements and plasma parameters from ELM-free, MHD quiescent H-modes were gathered in a database
Database details
129 entries from 29 discharges
  BT0 = 4.5 kG
  Ip = 700-900 kA
  15-45 ms averaging
Turbulence parameters
  Lc/ri ~ 12
  kqri ~ 0.2
  td/(a/cs) ~ 5
  tdw*pi ~ 0.15
Plasma parameters
  generally 50%-300% variation
  ne, ∇ne, Te, ∇Te, Ti, ∇Ti, vt, ∇vt, q, ŝ, ne, ni, b, be, nped, DRped, drsep

## Slide 17: A search algorithm identifies linear regression models that show similar scalings despite different parameter compositions
Algorithm adds or removes xk in model to find local minimum in model error
Many local minima exist in high dimensional xk space
Screen models for statistical quality to identify “good” models
  Statistical significance (ak t-statistics)
  Multicollinearity (variance inflation factor)
  Error normality (Studentized residuals)
plasma
parameters
scaling
coefficient
turbulence
parameters
Linear regression models exhibit similar scalings despite different parameter compositions

## Slide 18: Lc increases at higher ∇ne, 1/LTe, n, and nped; decreases at higher Ti, ∇Ti, and ∇vt
Consistent scalings
emerge from different regression models

## Slide 19: kq scalings consistent with Lc scalings; td scalings provide additional insight

## Slide 20: Scalings point to a variety of turbulence mechanisms
Parametric scalings point to enhanced turbulence structures (larger Lc and td) at higher ∇ne and 1/LTe
  Possibly TEM turbulence
∇vt scalings for Lc and kq point to turbulence suppression
  Equilibrium E×B flow shear
ne and ni scalings for Lc and kq are consistent with zonal flows
  td decreases with ne
Pedestal height (nped) increases at larger Lc and td
  Consistent with larger structures and wider pedestals

## Slide 21: Post-ELM harmonic features at 50-100 kHz are localized at the top of the pedestal
Harmonic features are either absent from or weakly present in magnetic spectra

## Slide 22: TAE and GAE mode structures have been observed in extended radial regions
GAE mode
TAE burst
with A. Bortolon and W. Heidbrink
with K. Tritz

## Slide 23: Directions for future work
Big picture goal: validate plasma turbulence and transport models in core and edge regions
Quantify fluctuation amplitudes and radial correlation lengths
Study pre- and post-LH transition
  Turbulence spreading from edge to core
Measure flow fluctuations and flow shear
  Study flow fluctuations and shear across LH transition
  Identify role of zonal flows and mean flow
Identify post-ELM harmonic oscillations
  Captured by peeling-ballooning model?
  Connect to DIII-D observations and edge harmonic oscillations

## Slide 24: Summary: We measured pedestal turbulence quantities and identified parametric dependencies in ELM-free, MHD quiescent H-mode plasmas
The BES system on NSTX provides localized density fluctuation measurements with core-to-edge radial coverage
The BES system has measured poloidal correlation length, wavenumber, and decorrelation time of pedestal turbulence
Regression models identify parametric scalings and point to a variety of turbulence mechanisms
  Enhanced turbulence structures at higher ∇ne and 1/LTe
  ∇vt scalings point to E×B turbulence suppression
  Collisionality scalings for Lc and kq are consistent with zonal flows
  Pedestal height increases at longer Lc and td
Other observations
  Reduced turbulence at LH transition
  Post-ELM harmonic oscillations
  TAE and GAE mode structure