## Slide 1: Vacuum ultraviolet and Ultraviolet Spectrometers for Real-time Radiative Divertor Feedback Control in the NSTX-U Tokamak
V. A. Soukhanovskii, R. Kaita, B. Stratton, and NSTX-U Team
Madison, WI, 5-9 June 2016, 2016

## Slide 2: Abstract
To prevent excessive erosion and thermal damage of divertor plasma-facing components, a radiative divertor technique is planned for the NSTX-U tokamak. In the radiative (partially detached) divertor, plasma volumetric power and momentum losses are significantly increased by means of extrinsically seeded deuterium or impurity gases. A real-time feedback control of the gas seeding rate (the actuator) is planned. The control sensors can include a variety of diagnostics; however, to make the radiative divertor control independent of main plasma discharge parameters (e.g., input power, plasma current, density, seeding gas, etc), we consider divertor plasma electron temperature as a control parameter. During divertor detachment, a radiation front is formed at 10-15 eV if low-Z impurities (e.g., carbon, nitrogen) are used for radiation. In the strike point region, strong deuterium high-n Balmer and Paschen series line emissions are observed. A vacuum ultraviolet spectrometer SPRED with a fast camera detector is developed for temperature monitoring at Te < 15 eV, based on the Dn=0,1,2 line intensity ratios of low-Z lines in the spectral range 300-1600 A. A separate multichannel ultraviolet spectrometer is used for temperature measurements based on the Balmer line intensities at Te < 5 eV. Both spectrometers use collisional-radiative model based line intensity ratio interpretation and output a real-time Te-dependent signal within a characteristic divertor detachment equilibration time of ≤ 15 ms.
Prepared under Contracts DE-AC52-07NA27344 and DE-AC02-09CH11466.

## Slide 3: Outline
Radiative divertor technique in standard and snowflake configurations are leading heat flux mitigation candidates in NSTX-U
Real-time Te from two spectrometers is proposed as control signal for radiative divertor control
  VUV spectrometer SPRED – carbon and nitrogen ion emission lines for 5 eV ≤ Te ≤ 25 eV
  UV spectrometer DIBS – deuterium Balmer lines and recombination continuum for Te ≤ 0.5-3 eV

## Slide 4: Various techniques developed for reduction of heat fluxes q|| (divertor SOL) and qpeak (divertor target)
Divertor peak heat flux mitigation techniques:
Divertor geometry (poloidal flux expansion, divertor plate tilt, magnetic balance, snowflake divertor)
Radiative divertor with extrinsic impurity seeding
Radiated power loss
Increase via Vdiv, LII
Poloidal target
inclination, up-down,
in-out fractions,
N divertors
Increase plasma-wetted area
Increase lq via
increased
radial transport, LII
Increase divertor area at large RSP
Increase plasma-wetted area via increasing fexp

## Slide 5
Open geometry divertor with graphite PFCs will be used in initial years in NSTX Upgrade
New center-stack
2nd neutral beam
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
J. E. Menard et. al, Nucl. Fusion 52 (2012) 083015
Open divertor geometry
No active divertor pumping
Graphite plasma facing components
Four up-down symmetric divertor coils
Diagnostics: IR cameras, MPTS, Langmuir probes, filtered visible cameras, VUV-UV-VIS-NIR spectroscopy
Gas

## Slide 6: Edge modeling predicts significant heat flux reduction with radiative snowflake divertor
Snowflake with 3% carbon
Wide density operational window as low as ne/nG≤0.4
  Peak heat flux reduced up to 50% stronger (cf. standard radiative divertor) at lower ne
  Less impurity seeding (argon or neon) needed for lower peak heat flux
Multi-fluid code UEDGE
  Bt = 1.0 T, Ip = 2 MA, PSOL = 9 MW
  NSTX-like transport χi,e=2-4 m2/s, D=0.5 m2/s
Standard Snowflake
Total
Rad.
heating
E. T. Meier et. al, Nucl. Fusion (2015)

## Slide 7: Impurity-seeded radiative divertor with feedback control is planned for long discharges
In NSTX, heat flux reduction in radiative divertor compatible with H-mode confinement was demonstrated with D2 or CD4 puffing
Feedback control of divertor radiation via impurity particle balance control
  Cryopump for particle removal
  Divertor gas injectors
  Real-time control signal diagnostics could include
    PFC temperature via IR thermography or thermocouple
    Thermoelectric current between inner and outer divertor
    Impurity VUV spectroscopy or bolometry
    Neutral gas pressure or electron-ion recombination rate
    Spectroscopic Te estimation
Soukhanovskii, HTPD 2012, RSI 2012

## Slide 8: Conceptual design of radiative divertor feedback control system is based on PID control
Proportional, integral, derivative controller

## Slide 9: Control actuator – the new divertor gas injection system is being commissioned
Four ½” OD SS divertor gas injection lines
2 upper and 2 lower
  Copper backing plates modified to run tubing
  Piezoelectric valves located at L=50 ms x vc from orifice
  G ≤ 1e22 particles/s

## Slide 10: Te-sensitive line intensity ratios are considered for divertor detachment control signal
Balmer n=6-12 series lines in ion-neutral interaction zone Te ≤ 5 eV
  Population kinetics is dominated by 3-body recombination at lower temperature
  3-body recombination rate
  R ~ ne3 Te-4.5
  Plasma is optically thin for Balmer lines
  Dominated by Stark broadening due to linear Stark effect in electron and ion microfield. Other mechanisms neglected: Zeeman spitting, Van der Waals and natural broadening
  Background due to bremsstrahlung and radiative recombination
Figure concept after M. E. Fenstermacher, PPCF 1999
Carbon or nitrogen Dn=0; 1; 2 lines in impurity radiation zone Te ≤ 10-15 eV
  Intensity ratios highly Te sensitive due to Te sensitivity of excitation rates
  Emission also proportional to impurity density

## Slide 11: Carbon or nitrogen Li-like and Be-like ion Dn=0; 1; 2 line intensity ratios are Te sensitive
Dn=0 and Dn=1 are baseline approach
Dn=2 transitions can also be considered if reliably measured
ADAS PECs used (PEC93)
 Lines correspond to three densities 2, 5, 20 x 1019 m-3

## Slide 12: Divertor SPRED spectrometer has broad applications for NSTX-U program
Support plasma-facing component program
  Steady-state and transient divertor impurity measurements
    edge / divertor Mo III-XIV line emission
    SOL / divertor Li II, Li III, C II, C III, C IV line emission
Support divertor program
  Divertor carbon ionization balance (steady-state and during ELMs)
  Divertor Te estimates from C II, C III, C IV line ratio (LR) measurements
    Deviation from Maxwellian EEDF might be detected from these LR’s
  Improved divertor Prad analysis
    Most Prad is due to several strong C III - C IV emission lines in the VUV
  Radiative divertor impurity radiation (CD4, N2, Ne, Ar)
  Detached divertor Lyman series for recombination rate, Te, opacity

## Slide 13: Divertor SPRED VUV spectrometer enables impurity emission measurement in outer divertor leg

## Slide 14: VUV spectrometer SPRED
McPherson Model 251 flat-field 0.3 m spectrograph (Weight: 250 lb)
Two-grating turret with Au-coated gratings 290 and 2105 l/mm
MCP-based detector with CsI-coated photocathode and P46 phosphor
  Time response 50 um
Ion pump with controller
Schott 12 ft imaging bundle 25x4 mm
Princeton Instruments Pro-EM 1600x200 camera
  Electron multiplication gain 1-1000
  16 um pixels
  Readout time if fully vertically binned 0.70 ms
  Readout time if single row 0.22 ms

## Slide 15: Laboratory spectral measurements with divertor SPRED
Hamamatsu VUV D2 lamp
Laboratory SPRED measurements performed through a MgF2 window – hence the cut-off at about 1150 A
Laboratory measurements show high dynamic range of the detector system
Spectral range 200-1600 A is adjusted and confirmed

## Slide 16: Micro-channel plate gain and phosphor acceleration ranges are verified in the laboratory
MCP + CCD tested with Hamamatsu VUV D2 lamp
Spectral feature at 1260 A is used
MCP gain varies over 2.5 orders of magnitude
Phosphor acceleration can also be varied by factor 10

## Slide 17: NBS 1963A Optical resolution target test shows 30 um spatial resolution of optical relay and detector system
High-frequency NBS 1963A resolution test targets
Target attached to fiberoptic bundle, lens and CCD
Resolution about 30 um

## Slide 18: CRETIN code modeling used for Te sensitivity of D, Li, C spectra
CRETIN code is a collisional-radiative and radiation transport solver
  H. Scott, J. Quant. Spectrosc. Radiat. Transf. 71 (2001) 689
  Calculates whole spectrum including bremsstrahlung, line emission,line profiles, self-absorption, ionization and recombination
  Includes NLTA population kinetics, radiation transport, neutral diffusion, diagnostic simulators
  Line profiles code: TOTAL
    Quasi-static approximation for ions, impact approximation for electrons
    Electric dipole momentum reduced matrix elements must be calculated elsewhere
Atomic data either from FAC or from hydrogenic model

## Slide 19: Li, C, O spectra simulations with CRETIN demonstrate feasibility of spectroscopic Te measurements
l (nm)

## Slide 20: High-n Balmer line spectra used in NSTX for divertor recombination rate, Te and ne studies
Balmer series spectra modeled with CRETIN
Te=0.8-1.2 eV, ne=2-7 x 1020 m-3 inferred from modeling
Free-bound continuum modeled with CHIANTI
V. A. Soukhanovskii et al., Nucl. Fusion 2011
V. A. Soukhanovskii et al., RSI 2006

## Slide 21: Cretin UV spectra simulations demonstrate feasibility of spectroscopic Te measurements
S

## Slide 22: Te is estimated from Balmer line intensity ratio and from continua intensity ratio at Paschen jump
l (nm)

## Slide 23: Divertor imaging optics enables quasi-2D divertor emission measurements in UV-VIS-NIR
26-fiber bundle (Radiation resistant Molex FVP 200 um)
10-fiber bundle (Molex FBP 200 um)
30 m length
Kogaku 8 or 12 mm imaging UV lens
Fiber projection spot size 2-6 mm
FVP
FBP

## Slide 24: Divertor Imaging Balmer Spectrometer (DIBS) enables fast line and continua measurements
SCT 320 Czerny-Turner-Schmitt spectrograph
  600, 1200, 1800 gr/mm UV-VIS 68 mm gratings
CCD camera PI ProEM 1600x400
Real-time DAQ via WinSpec32 (pvcam)
Grating l/mm | CWL | Range (nm) | Short wl | Long wl | Dispersion nm/mm | CCD resolution (FWHM) | Bandwidth per pixel
600 | 399 | 124 | 336 | 461 | 4.849 | 0.14 | 0.078
1200 | 380 399 | 59 59 | 350 369 | 409 428 | 2.333 2.321 | 0.067 0.067 | 0.037 0.037
1800 | 399 | 37 | 380 | 417 | 1.452 | 0.044 | 0.023