## Slide 1: Developing snowflake divertor physics basis in the DIII-D and NSTX tokamaks.
1st IAEA Technical Meeting on Divertor Concepts
1 October 2015
Vlad Soukhanovskii

## Slide 2: Acknowledgements
S.L. Allen1, M.E. Fenstermacher1, C.J. Lasnier1,M.A. Makowski1, A.G. McLean1, E.T. Meier1, W.H. Meyer1, T.D. Rognlien1, D.D. Ryutov1, F. Scotti1, E. Kolemen2, R.E. Bell2, A. Diallo2, S. Gerhardt2, R. Kaita2, S. Kaye2, B.P. LeBlanc2, R. Maingi2, J.E. Menard2, M. Podesta2, A.L. Roquemore2, R.J. Groebner3, A.W. Hyatt3, A.W. Leonard3, T.H. Osborne3, T.W. Petrie3, J.-W. Ahn4, R. Raman5, and J.G. Watkins6
1 Lawrence Livermore National Laboratory, 7000 East Ave, Livermore, CA 94550, USA
2 Princeton Plasma Physics Laboratory, PO Box 451, Princeton, NJ 08543-0451, USA
3 General Atomics, PO Box 85608, San Diego, CA 92186-5608, USA
4 Oak Ridge National Laboratory, Oak Ridge, TN 37831, USA
5 University of Washington, Seattle, WA 98195, USA
6 Sandia National Laboratories, PO Box 969 Livermore, California 94551-0969, USA

## Slide 3: Divertor strike point heat flux mitigation using radiated power loss and magnetic geometry
Divertor physics is inherently 2D or even 3D
  Parallel / cross-field transport and turbulence
  Radiation front (detachment) stability
  Neutral pressure / density distribution
Important engineering aspect – divertor coil layout
Radiated power loss
Increase via Vdiv, LII
Poloidal target inclination, up-down, in-out fractions,
N divertors
Increase plasma-wetted area
Increase lq via
increased
radial transport, LII
Increase divertor area at large RSP
Increase plasma-wetted area via increasing fexp

## Slide 4: Focus on divertor power exhaust via geometry since early days of tokamak studies. Some examples…
D. D. Ryutov, J. Plasma Phys. 2015, 81, 495810516
H. Takase, J. Phys. Soc. J. 70, 609, 2001
M. Kotschenreuther et. al, IAEA FEC 2004; Phys. Plasmas 14, 072502 (2007)
B. Badger et.al, U. Wisc. Report UWFDM-150, 1975
F. H. Tenney,
PPPL Report 1284, 1976
N. Ohyabu et. al, Nucl. Fusion 5 519 (1981)
P. M. Valanju et.al, Phys.
Plasmas 16, 056110 (2009)
B. LaBombard et.al, NF 55 (2015) 053020
R. A. Pitts et. al, JNM 290-293, 2001, 940
UWMAK-III
Double-null with long legs
Expanded
Boundary,
Doublet III
Super-X
TCV
Cusp-like
X-divertor
X-point
divertor
Super-cusp with
Remote coils

## Slide 5: Snowflake Divertor Configuration as a Tokamak Divertor Power Exhaust Concept
D. D. Ryutov, PoP 14, 064502 2007;
PPCF 54, 124050 (2012)
Snowflake, 2nd order null
  Bp ~ 0, grad Bp ~ 0
    (Cf. first-order null: Bp ~ 0)
  Bp(r)~r2 (Cf. first-order null: Bp ~ r )
  Four divertor legs
Geometry benefits
  Higher edge magnetic shear
  Larger plasma wetted-area Awet (fexp)
  Larger parallel connection length L||
  Larger effective divertor volume Vdiv
To maximize geometry benefits: dXX ≤ a (lq /a)1/3
Transport benefits
  High convection zone with radius D*
  Power sharing over four strike points
  Enhanced radial transport (larger lq)
To maximize sharing: dXX ≤ D*~a (a bpm / R)1/3

## Slide 6: Snowflake configurations obtained in NSTX and DIII-D using existing PF coils for many energy confinement times
NSTX
  Ip=0.8-1.0 MA
  Bt≤0.45 T
  3 divertor coils, pre-programmed currents
  SF for 0.5 s
DIII-D
  Ip=0.8-1.0 MA
  Bt=2 T
  3 divertor coils w/control
  SF for 2-3 s
Next slides: Attempt to generalize snowflake divertor effects observed in NSTX and DIII-D

## Slide 7: Snowflake divertor compatible with H-mode core and pedestal confinement, effect on ELMs vary
SF Divertor Weakly Affects Pedestal Magnetic and Kinetic Characteristics, Peeling-ballooning Stability in DIII-D
SF divertor strongly affects pedestal peeling-ballooning stability in NSTX, destabilizes ELMs
Snowflake
Standard

## Slide 8: Peak divertor heat flux significantly reduced due to snowflake divertor geometry effects
Due to geometry and radiation
Standard Snowflake
Flux expansion increased ~20%
L|| increased by 20-60% over SOL width
Divertor heat flux reduced ~40%
SOL width
Snowflake
Standard
q_div (MW/m^2)

## Slide 9: Snowflake divertor enables power and particle sharing over multiple strike points
GSP3
qSP3
qSP1
Standard Snowflake
Increased lq may imply increased transport
lq = 2.40 mm
lq = 3.20 mm
SP1 Parallel heat flux (MW/m2)

## Slide 10: Snowflake configuration favorably affects radiative divertor and detachment
Radiative Radiative
Standard Snowflake
PSOL = 3-4 MW
Natural partial detachment in NSTX snowflake otherwise inaccessible with standard divertor
Significant radiated power re-distribution
Decreased near null, increased through leg
PSOL = 2-3 MW
Nearly complete power detachment
Radiative Radiative
Standard Snowflake

## Slide 11: Snowflake divertor reduces ELM energy and divertor surface heating (peak heat flux)
Divertor heat flux significantly reduced during Type-I ELMs (DW/W ~ 5-15 %)
Both DWELM and DWELM/Wped weakly reduced
Mostly for DWELM/Wped < 0.10
DTsurf~EELM/(Awet tELM )1/2
Increased tELM=LII/cs,ped
  Weakly reduced EELM
  AwetELM similar
Standard Snowflake
Standard Snowflake
T. D. Rognlien et. al,
JNM 438, 2013, S418

## Slide 12: Developing the Snowflake Divertor Physics Basis For High-power Density Tokamaks
SF divertor configurations compatible with high H-mode confinement and high pressure pedestal
Snowflake geometry may offer multiple benefits for inter-ELM and ELM heat flux mitigation
  Geometry enables divertor inter-ELM heat flux spreading over larger plasma-wetted area, multiple strike points
  Broader parallel heat fluxes may imply increased radial transport
  ELM divertor peak target temperature and heat flux reduction, especially in radiative snowflake configurations

## Slide 13: First pre-DEMO and DEMO device designs with snowflake divertor configurations
Y. Wan, SOFE 2013
CFETR
Z. Luo et.al, IEEE TRANSACTIONS ON PLASMA SCIENCE, V42, 2014, 1021
R Albanese et. al,
PPCF, 56 (2014) 035008
Snowflake for DEMO
N. Asakura et.al,
Trans. Fus. Sci. Tech. 63, 2013, 70.
Snowflake for DEMO
Snowflake for DEMO

## Slide 14: Backup

## Slide 15
Snowflake divertor is a leading heat flux mitigation candidate for NSTX Upgrade
New center-stack
2nd neutral beam
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
NSTX-U Mission elements:
  Advance ST as candidate for Fusion Nuclear Science Facility
  Develop solutions for the plasma-material interface challenge
  Explore unique ST parameter regimes to advance predictive capability for ITER
  Develop ST as fusion energy system
J. E. Menard et. al, Nucl. Fusion 52 (2012) 083015
  New divertor coil
  Upper-lower snowflake divertors
  Supported by NSTX-U divertor coils and compatible with coil current limits

## Slide 16
Snowflake divertor is a leading heat flux mitigation candidate for NSTX Upgrade
New center-stack
2nd neutral beam
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
NSTX-U Mission elements:
  Advance ST as candidate for Fusion Nuclear Science Facility
  Develop solutions for the plasma-material interface challenge
  Explore unique ST parameter regimes to advance predictive capability for ITER
  Develop ST as fusion energy system
J. E. Menard et. al, Nucl. Fusion 52 (2012) 083015

## Slide 17: Edge modeling predicts significant heat flux reduction with radiative snowflake divertor
  Snowflake with 3% carbon
    Wide density operational window as low as ne/nG≤0.4
    Peak heat flux reduced up to 50% stronger (cf. standard radiative divertor) at lower ne
  Less impurity seeding (argon or neon) needed for lower peak heat flux
  Multi-fluid code UEDGE
  Bt = 1.0 T, Ip = 2 MA, PSOL = 9 MW
  NSTX-like transport ci,e=2-4 m2/s, D=0.5 m2/s
Standard Snowflake
Total
Rad.
heating
E. T. Meier et. al, Nucl. Fusion (2015)

## Slide 18: Advanced divertor magnetic configurations (classified by appearance)
Multiple divertors, each with one X-point
Higher order (2nd, 3rd) null divertors
Divertor with multiple X-points
Long-legged divertors with multiple X-points
Note on early concepts
  Envisioned before H-mode discovery (1982)
  Some concepts envisioned divertor for particle and impurity control only

## Slide 19: 1. Multiple divertors: triple-null, quadruple-null to share heat and particle fluxes
D-shaped plasma, high triangularity
Increased local shear
Enhanced kink stbility
J. Kesner, Nucl. Fusion 30, 548 (1990)
K. Bol et.al, Nucl. Fusion 25, 1149 (1985)
Poloidal Divertor Experiment tokamak at PPPL (1979 – 1983)
Significant contribution to divertor physics with double-null configuration

## Slide 20: 2. Higher order null divertors : larger region of very low Bp to affect geometry and transport
Snowflake, 2nd order null
  Bp ~ 0, grad Bp ~ 0 (Cf. first-order null: Bp ~ 0)
  Bp(r)~r2 (Cf. first-order null: Bp ~ r )
  Four divertor legs
Cloverleaf, 3rd order null
  Bp(r)~r3
  Six divertor legs
Strong plasma convection
D. D. Ryutov, Phys. Plasmas 14 (2007), 064502
D. D. Ryutov et. al, Phys. Plasmas 20 (2013), 092509

## Slide 21: 3. Divertor with multiple X-points: expand SOL in the divertor region
Poloidal Bundle + Expanded Boundary
Analysis of radiation, H-mode compatibility, neutron shielding, coil currents
N. Ohyabu, J. Plasma Fus. Res. 5 525 (1991)
N. Ohyabu et. al, Nucl. Fusion 5 519 (1981)
Doublet III Expanded Boundary

## Slide 22: 3. Divertor with multiple X-points: expand SOL in the divertor region
Cusp-like divertor configuration
  Coil currents acceptable for ITER-like parameters
H. Takase, J. Phys. Soc. J. 70, 609, 2001
M. Kotschenreuther et. al, IAEA FEC 2004;
Phys. Plasmas 14, 072502 (2007)
X-Divertor
  Small dipole coils under each divertor leg, inside the TF
  Potential to stabilize rad. front

## Slide 23: 4. Long-legged divertors with multiple X-points: increase connection length, expand SOL
F. H. Tenney et.al,
J. Nucl. Mater. 53 43 (1974)
Conceptual divertor design for Princeton Reference Design Reactor.
A.V. Georgievsky et.al, 6th Symp Eng Prob of Fus Energy, p 583, 1975, IEEE 75CH1097-5-NPS, Copyright 1976
F. H. Tenney,
PPPL Report 1284, 1976
Long-legged double null poloidal divertor
Long-legged high flux expansion poloidal divertor

## Slide 24: Long-legged divertors with multiple X-points
R. W. Conn et.al, U. Wisc. Report UWFDM-114, 1974
B. Badger et.al, U. Wisc. Report UWFDM-150, 1975
G. L. Kulcinski et.al, U. Wisc. Report UWFDM-173, 1976
UWMAK-II
UWMAK-III
Tokamak Enginering Test Reactor
UW Fusion Technology Institute conceptual reactor systems studies

## Slide 25: 4. Long-legged divertors with multiple X-points
D. Meade, Private Communication
T. F. Yang et.al, Westinghouse Corp. WFPS-TME-055 1977
TNS reactor (w/ ORNL)
Divertor heat flux 1-3 MW/m2
Flowing liquid lithium targets for heat and particle removal
PDX Modification proposal

## Slide 26: 4. Long-legged divertors remove interaction zone away from plasma
Conceptual design Engineering Test Facility
R=5.6 m
a=1.3 m
Bt=5.5 T
Ip=6.1 MA
PNBI=60 MW
Poloidal divertor
  W target plates
  Cryo-panels for particle control
P. H. Sager et. al, J. Vac. Sci. Tech. 18, 1081 (1981)

## Slide 27: 4. Long-legged divertors with multiple X-points
M. Peng, Steady-state Spherical tokamak TST,
Workshop on Edge Plasma for BPX and ITER, 1991
B. LaBombard et.al, APS 2013,
IAEA 2014
P. M. Valanju et.al, Phys.
Plasmas 16, 056110 (2009)
Super-X divertor
X-point target divertor
ADX tokamak proposal

## Slide 28: Advanced magnetic divertor configurations: status of experiments
Dedicated experimental devices (1979-1986)
    PDX
    Doublet III Expanded boundary
Snowflake divertor configuration (existing devices with existing coils, 2008-present)
    TCV, 2008
    NSTX, 2009
    DIII-D, 2012
    EAST, 2014
Long leg divertor physics (2010-present)

## Slide 29: 1. Doublet III Expanded Boundary was the first advanced magnetic divertor configuration experiment
Stability of divertor configuration with outside PF coils
Integrated power and particle exhaust
  Reduction of intrinsic impurities in the core
  Radiative divertor plasma cooling with seeded argon
  Argon screening from main plasma
Compatibility with core confinement
A. Mahdavi et. al, J. Nuc. Mater. 111 (1982) 355
N. Ohyabu et. al, Nucl. Fusion 5 519 (1981)

## Slide 30: Snowflake divertor configurations obtained with existing divertor coils, maintained for up to 10 tE

## Slide 31: Snowflake divertor configurations obtained with existing divertor coils in NSTX

## Slide 32: Impulsive heat loads due to Type I ELMs are mitigated in snowflake divertor
H-mode discharge, WMHD ~ 220-250 kJ
  Type I ELM (W/DW ~ 5-8 %)
Steady-state At ELM peak

## Slide 33: NSTX: Access to radiative detachment with intrinsic carbon in snowflake divertor facilitated
Snowflake divertor (*): PSOL~3-4 MW, fexp~40-60, qpeak~0.5-1.5 MW/m2
  Low detachment threshold
  Detachment characteristics comparable to PDD with D2 or CD4 puffing

## Slide 34: Increased Plasma-wetted Area Leads to qpeak Reduction In Snowflake Divertor
Snowflake with dXX < 10 cm
Core plasma unaffected
  5 MW NBI H-mode
  Stored energy and density constant
Divertor power balance unaffected
In outer divertor, qpeak reduced by 30%
Standard Snowflake

## Slide 35: Detailed ELM Analysis: DW(ELM) decreased, W pedestal constant in SF
Detailed ELM analysis before/during SF shows:
Pedestal Energy (WPEDESTAL) Constant
Confinement Constant
Change in stored energy lost per ELM (ΔWELM) is reduced
Consistent with Loarte connection length scaling
S. L. Allen et al., Paper PD/1-2, IAEA FEC 2012.

## Slide 36: qpeak Reduction in Snowflake Divertor Partly Due to Increased Awet and L||
Flux expansion increased ~20%
  Depends on configuration, can be up to X3
L|| increased by 20-60% over SOL width
Divertor heat flux reduced ~30%
Parallel heat flux reduced ~20%
SOL width
Standard Snowflake
Strike
point

## Slide 37: Convective Plasma Mixing Driven by Null-region Instabilities May Modify Particle and Heat Transport
  Flute-like, ballooning and electrostatic modes are predicted in the low Bp region
  bp=Pk/Pm = 8p Pk/Bp2 >> 1
  Loss of poloidal equilibrium
  Fast convective plasma redistribution
  Especially efficient during ELMs when Pk is large
Estimated size of convective zone
  Standard: 1 cm
  Snowflake: 6-8 cm
D. D. Ryutov, IAEA 2012; Phys. Scripta 89 (2014) 088002.
Divertor null-region bp measured by divertor Thomson Scattering
  In snowflake, broad region of higher bp>>1
  Higher X10 during ELMs

## Slide 38: Broader q|| Profiles in Snowflake Divertor May Imply Increased Radial Transport
Fit q|| profile with Gaussian (S) and Exp. (lSOL) functions (Eich PRL 107 (2011) 215001)
Increased lq may imply increased transport
  Increased radial spreading due to L||
  SOL transport affected by null-region mixing
  Enhanced dissipation may also play role
lq = 2.40 mm
lq = 3.20 mm
Standard Snowflake
Parallel heat flux (MW/m2)

## Slide 39: Peak divertor heat flux significantly reduced due to snowflake divertor geometry effects
Geometry and radiation
Standard Snowflake
Flux expansion increased ~20%
L|| increased by 20-60% over SOL width
Divertor heat flux reduced ~40%
SOL width
Snowflake
Standard
Inner SP
Outer SP