## Slide 1: Nyquist analysis of kinetic effects on the plasma response in NSTX and DIII-D experiments
26th IAEA Fusion Energy Conference
Kyoto, Japan
October 17-22, 2016
Z.R. Wang1
Y.Q. Liu2, J.-K. Park1, M.J. Lanctot3, C. Paz-Soldan3, Y.W. Sun4 and J. Menard1
        1) Princeton Plasma Physics Laboratory, Princeton, NJ 08543, USA
        2) CCFE Culham Science Centre, OX14 3DB, UK
        3) General Atomics, San Diego, CA 92101, USA
        4) Institute of Plasma Physics, Chinese Academy of Science, Hefei, China

## Slide 2: Motivation
Externally applied non-axisymmetric magnetic perturbations strongly modify tokamak plasmas with perturbed plasma currents plasma response (include magnetic perturbation and plasma displacement etc.)
Physics understanding for plasma response closely relate to many subjects
  Neoclassical toroidal viscosity, Error fields control, Resistive wall mode instability, ELM suppression etc.
Nyquist analysis, combined with Padé approximation, can provide a deep physical understanding of the plasma response.
  how kinetic effects fundamentally change eigenmodes in DIII-D and NSTX plasmas. Note plasma response is the result of the linear combination of stable eigenmodes
  quantify contribution of each eigenmode in order to characterize details of the multi-modal plasma response
  better understand the plasma response during ELM supression
Z. R. Wang, M. J. Lanctot et al PRL 2015

## Slide 3: Linear Simulation of Plasma Response: Hybrid Drift-Kinetic MHD Formulation (MARS-K)
Resonant operator in :
MARS-K extends MARS-F and solves linearized MHD equations with perturbed kinetic pressure.
Y.Q. Liu et al, PoP 2008
Fluid Part (MHD equations):
Diamagnetic drift
Applied field
frequency
Precession
drift
Bounce/Transit
EXB
Crook
Collisions
Kinetic pressure and couple with MHD equations
replaced by kinetic pressure
Coil equations:
Applied field frequency
Drift-kinetic equation:
: perturbed Lagrangian
Ignore finite orbit width effect.
Drift kinetic effects can modify plasma response.
Kinetic Model

## Slide 4: Nyquist Analysis and Pad Approximation
The standard Nyquist contour involves varying the field rotation frequency, , generated by external magnetic perturbation coils from -∞ to +∞, where the ‘+’ and ‘-’ denotes the co and counter plasma current directions.
The real and imaginary parts of the total radial perturbed magnetic fields measured by toroidal arrays of magnetic sensors can be plotted in the complex plane to form the Nyquist contour.
Nyquist contour can be fitted by Pad approximation to extract the plasma transfer functions and the eigenvalue.
Considering the generalized form of linearized MHD equations,
C is the driving term of coil, the form of transfer function on given sensor is
Sensor transfer function:
is the eigenvalue of each eigenmode.

## Slide 5: Frequency Scan of Plasma Response in DIII-D and NSTX with Different Coil Configurations
Magnetic perturbation can be generated by I-coils in DIII-D and the external coil in NSTX.
By scanning the rotating frequency of external field, Nyquist contour can be formed by plotting the magnetic sensor measurement in complex plane.
Center stack casing
Magnetic
sensor
Resistive
Wall (MARS)
NSTX configuration
External
coil
Passive
plate
Vacuum vessel
DIII-D configuration
Resistive
Wall (MARS)
NSTX-U
MPID1A
MPID1B

## Slide 6: NSTX: Kinetic Plasma Response With Thermal Particles Shows Quantitative Agreement with Magnetic Sensor Measurements
The simulated plasma response is compared with experiments at upper radial magnetic sensor.
1) Fluid plasma response is solved by MARS-F
2) Kinetic plasma response is solved by MARS-K (include thermal ions and electrons).
3) Fluid plasma response is solved without resistive wall
NSTX f= - 30Hz
~ 4.75
Fluid
no wall
Kinetic
NSTX f=30Hz
~ 4.75
Fluid
no wall
Kinetic
Fluid
with wall
Fluid
with wall
NSTX-U

## Slide 7: NSTX: Inertial Energy Plays a Destabilizing Role in NSTX Plasmas Response
Momentum equation:
Inertial energy is negative and destabilizes the plasma which leads to larger amplification of plasma response.
NSTX f=30Hz
~ 4.75
With fluid flow
Without fluid flow
Inertial
Coriolis force
Centrifugal force
(a.u.)
NSTX-U

## Slide 8: NSTX Shows Strong Plasma-Wall Coupling Effect in n=1 Plasma Response
A simple analysis based on (s, ) model in the approximation with a single dominant mode:
At marginal stability:
Park, Boozer et al, PoP 2009
No wall:
=3.5ms, =+/-30Hz, =1.52
strong plasma-wall coupling
NSTX f=30Hz
~ 4.75
Fluid
no wall
Kinetic
Fluid
with wall
NSTX experiments
NSTX-U

## Slide 9: NSTX: Bounce and Transit Resonances of Thermal Ions Contributes Dominant Kinetic Energy to Kinetic Response
To understand which drift kinetic effect of thermal particles play a role to change the plasma response, the perturbed drift kinetic energy is analyzed near no-wall beta limit in NSTX plasmas.
Thermal electrons contribute much smaller due to high collision frequency, bounce frequency and transit frequency.
The fluid contour with rotation is similar to the kinetic contours since the physics of ion acoustic damping is dominant at high rotation. The ion acoustic damping is the fluid description of the kinetic resonance of passing ions.
NSTX f=30Hz
NSTX discharge 124801 at 560ms
(a.u.)
NSTX-U

## Slide 10: NSTX: Nyquist Contour Directly Identifies Kinetic Stabilization of Least Stable Mode in Plasma Response
Nyquist plot with highest beta above
Padé approximation:
Kinetic + Rotation
Kinetic w/o Rotation
Fluid + Rotation
Fluid w/o Rotation
Fluid w/o Rotation: = 13.66 Hz Unstable
Fluid + Rotation: = -28.97 Hz Stable
Kinetic w/o Rotation: = -34.3 Hz Stable
~ 4.75
Kinetic + Rotation: = -13.22 Hz Stable
Fluid ion acoustic damping
Inertial energy
NSTX-U
fcoil = 0Hz
fcoil = 10Hz

## Slide 11: DIII-D: Different Response Physics Form Different Nyquist Contour
Padé approximation:
Fluid w/o Rotation: = 79.24 Hz Unstable
Fluid + Rotation: = -20.44 Hz Stable
Kinetic w/o Rotation: = -9.19 Hz Stable
Kinetic + Rotation: = -8.69 Hz Stable
Fluid ion acoustic damping
~ 2.25
Nyquist plot with highest beta above
Kinetic + Rotation
Kinetic w/o Rotation
Fluid + Rotation
Fluid w/o Rotation
Z. R. Wang, M. J. Lanctot et al PRL 2015
fcoil = 0Hz
fcoil = 10Hz

## Slide 12: DIII-D: Multi-Mode Plasma Response in Kinetic-MHD Simulation (MARS-K) Quantified using Nyquist Contour Analysis
Scan rotation & calculate radial magnetic field at low field side of the wall
Low rotation => Single-mode response
High rotation => Multi-mode response
Use Padé approximation to extract eigenmodes
Yields damping rate for each stable mode
Quantifies contribution of each eigenmode to the total sensor signal
Instead of first least stable mode, contribution from second least stable mode can dominate the kinetic plasma response when largest response observed (~10Hz).
3rd mode
g = -77.7-12.24i (Hz)
2nd mode
g= -16.85+26.9i (Hz)
decreasing plasma stability
increasing plasma rotation
fcoil = 0Hz
fcoil = 0Hz
135759
fcoil = 10Hz
1st mode(stable)
g = -13.34-0.28i (Hz)
Choose the coil frequency to amplify the preferred eigenmode’s response.

## Slide 13: DIII-D: n=2 Plasma Response Results Show Multi-Mode Structure with Nyquist Analysis in Ideal MHD simulation (MARS-F)
ISL sensor
ESL sensor
UISL sensor
2nd mode(stable)
g ~ -53.4+ 2.5i (Hz)
1st mode(stable)
g ~ -18.4+1.92i (Hz)
Nyquist
Contour
fcoil = 10Hz
fcoil = 10Hz
fcoil = 10Hz
135759
Padé approximation indicates plasma is stable to n=2 modes in ideal MHD simulation.
Two mode contribute to fluid response.
Second least stable mode also dominates n=2 fluid plasma response.
Nyquist contour measured by different sensor can have different pattern.
Multi-mode
pattern

## Slide 14: Modified Pad Approximation Include Both Coil Phasing and Frequency Dependence
Standard Nyquist analysis requires a frequency scan .
Measurements at high frequency can be weak and noisy due to ELM etc.
Modified Nyquist Analysis: transfer function of Pad approximation is modified to include both frequency and phase dependence with two coils.
, =
Varying both coil phase difference and coil frequency reduces the requirement of frequency scan, no need to reach the high coil frequency.
Different sensor has the same eigenvalue (linear theory).
Avoid the resonance with mode and weak sensor signal at high frequency.

## Slide 15: DIII-D: Application of Modified Nyquist Method in n=2 plasma response experiments
The static field makes =0 at each sensor j:
The measurements of three sensors(MPID1A, MPID66M and MPID1B) are fitted by one pole (N=1) and three pole (N=3) models.
The data of n=2 magnetic measurements in [Paz-Soldan, Nazikian et al, PRL 114, 105001 (2015)] is used to exam modified Pad Approximation.
MPID1A sensor

## Slide 16: DIII-D: Application of Modified Nyquist Method in n=2 plasma response experiments
The measurements of three sensors(MPID1A, MPID66M and MPID1B) are fitted by one pole (N=1) and three pole (N=3) models.
MPID66M sensor
MPID1B sensor
Three poles model fits three sensors and confirms the multi-mode response.
Three eigenvalue can be found but not be able to determine the dimension since f=0.
=1.8696e+00 + 1.6963e+00i
8.5712e+00 - 1.9080e+00i
= 1.4569e-01 - 2.7639e-01i
No physical meaning

## Slide 17: DIII-D: Modified Transfer Function Fits Simulated n=2 Resistive Response at Different Phasing and Frequency
=10Hz
n=2 plasma response in DIII-D discharge 158103 at 3796ms is simulated by MARS-F.
Five pole transfer function fits the LFS and HFS sensor measurements simultaneously.
Radial perturbed fields at LFS (ISL)
Radial perturbed fields at HFS (Radial MPID1B)
O MARS-F
— Fitted
five pole
transfer
function
=90Hz

## Slide 18: DIII-D: Extracted Transfer Functions Identify Modification of n=2 Plasma Stability Due to Rotation and Resistivity
Case | Eigenvalue of Least Stable Mode
Ideal Response + no Rotation | -3.017 - 9.92E-03i Hz
Ideal Response + Rotation | -2.03 - 1.85E-03i Hz
Resistive Response + Rotation | -6.53 + 1.075E-02i Hz
Nyquist method can investigate how the damping rates of these stable eigenmodes in both simulation and experiments.
The extracted damping rates of least stable mode for ideal response with/without rotation and resistive response are compared.
DIII-D discharge 158103 at 3796ms
In the simulated DIII-D equilibrium, rotation slightly destabilize the plasma.
Resistivity plays a stabilizing effect on least stable mode.
More negative real part more stable plasma

## Slide 19: DIII-D: n=2 Response at HFS Purely Contributed by Plasma with Zero Degree Coil Phasing (Even Parity)
HFS (MPID1B)
Radial field
(a.u.)
Resistive response based on
DIII-D discharge 158103 at 3796ms
Extracted transfer functions from simulated vacuum response and total total response indicate pure plasma response has dominant contribution with even parity of I-coils in experiments.
ELM suppression appears near zero coil phasing.

## Slide 20: DIII-D: Least Stable Mode is Dominant in n=2 Resistive Plasma Response with Zero Degree Coil Phasing (Even Parity)
1st mode
=-6.5+0.01i Hz
2nd mode
=-61.9-0.0067i Hz
3rd mode
=-101.3+0.0045i Hz
4rd mode
=-113.8-3.07 Hz
5rd mode
=-822.5-0.014Hz
Least stable
mode
Least stable
mode
Least stable
mode
The least stable provides dominant contribution of plasma response.
Least stable mode has strongest amplification at 0 Hz when coil phasing is 0 deg.
DIII-D discharge 158103 at 3796ms
||
I
R

## Slide 21: MARS-F Simulation of Response for Modified Pad Approximation
EAST equilibrium (shot No. 52340) is used in the MARS-F simulation.
Phase scan of n=1 ideal response is simulated and measured by the assumed radial sensor at mid-plane of HFS.
Three contours with different coil frequencies (10Hz, 30Hz, 60Hz) are fitted at the same time.
Three poles model well fit the sensor signals to extract plasma transfer function.
f=10Hz
f=30Hz
f=60Hz
NSTX-U

## Slide 22: Two Modes Are Dominant on HFS with Zero Phase Degree
The eigenvalues of three poles：
  =-30.714 - 2.2163i Hz =-458.71 + 0.2993i Hz =-1624.8 + 3.02i Hz
The transfer function extracted from the low frequency and coil phase scan, can recover the simulated Nyquist contour at all frequency range.
Two modes are dominant (first and secondary modes)
Real
Imag
Abs
Frequency (Hz)
MARS-F
simulation
Extracted transfer
function
NSTX-U

## Slide 23: Use Transfer Functions to Optimize Coil Phase and Frequency for amplifying preferred eigenmode
Two dominant modes in fitted :
is amplified at 0 deg coil phasing. is amplified at 240 deg coil phasing.
Increasing coil frequency further enhances the amplification of mode which can be important during ELM suppression.
NSTX-U
Response transfer function:

## Slide 24: Nyquist Analysis Reveals Fundamental Contribution of Eigenmodes on Kinetic Plasma Response and Multi-Mode Response
Nyquist analysis is a powerful tool that can help to reveal a range of underlying physics associated with 3D fields. It finds
  dissipation of kinetic effects makes plasma more stable through stabilization of the eigenmodes.
  plasma in NSTX is destabilized by flow rotation and stabilized by eddy current in the wall.
  increasing EXB rotation can decrease the plasma stability in kinetic-MHD approach and make kinetic plasma response multi-modal.
  secondary mode can be dominant in n=1 kinetic response.
Modified Nyquist method including both coil phase and frequency dependences can
  indicate least stable mode plays a dominant role with zero degree coil phase in DIII-D n=2 ELM suppression experiments.
  give the capability to optimize coil phase and frequency for amplifying the preferred eigenmode during ELM control experiments e.g. amplify secondary mode with 240 degree coil phasing and finite coil frequency.
  be a candidate for 3D MHD spectroscopy and real-time monitoring of the plasma stability in long-pulse fusion reactors (new need high frequency scan to form Nyquist contour).
NSTX-U

## Slide 25: Frequency Scan of Each Eigenmode (n=2), no full cancellation among different modes