## Slide 1: Kinetic Resistive Wall Mode Stabilization Physics in Tokamaks
Jack Berkery
Columbia University
S.A. Sabbagh1, R. Betti2, H. Reimerdes3, J. Hanson1,
A. Balbaky1, R.E. Bell4, A. Diallo4, S.P. Gerhardt4, B.P. Le Blanc4, J.E. Menard4, M. Podesta4, Z.R. Wang4
1Columbia University, 2University of Rochester, 3Ecole Polytechnique Fédérale de Lausanne, 4PPPL
18th International Congress on Plasma Physics
Kaohsiung, Taiwan, June 27 – July 1, 2016
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: Outline
RWM Definition and Motivation
Kinetic Stability Theory
  Rotation
  Collisionality
  Energetic Particles
Comparison of Calculations and Experimental Results
Stability Estimation and Rotation Profile Control
Summary

## Slide 3: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
RWMs can cause a collapse in β, disruption, and termination of the plasma
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
unstable
stable
0

Ideal Kink
Mode

## Slide 4: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Bp
RWMs can cause a collapse in β, disruption, and termination of the plasma
NSTX 130235
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink
Mode
Resistive Wall Mode
~τw-1

Copper plate

## Slide 5: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Bp
RWMs can cause a collapse in β, disruption, and termination of the plasma
NSTX 130235
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink
Mode
Resistive Wall Mode
~τw-1

Copper plate

## Slide 6: A scalar critical plasma rotation model can not explain RWM stability; it depends on the ωφ profile
Early stability theories:
  Collisional dissipation of mode energy
  Rotational damping
    But models with scalar “critical rotation” for stability could not explain experiments
Plasma rotation
unstable
slowed by n=3 braking
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
Ideal Stability
Kinetic Effects
Unexplained experiments
New theory: consider kinetic effects
unstable RWM
NSTX
137722
140102

## Slide 7: Outline
RWM Definition and Motivation
Kinetic Stability Theory
  Rotation
  Collisionality
  Energetic Particles
Comparison of Calculations and Experimental Results
Stability Estimation and Rotation Profile Control
Summary

## Slide 8: “Kinetic effects” means taking into account complicated particle motion rather than treating the plasma as a fluid
Precession Drift
~ Plasma Rotation
Rotational resonance effect
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
MISK code
Solves for RWM growth rate
is solved by using from the drift kinetic equation
[R. Pitts et al., Physics World, March 2006
D. Pace et al., Physics Today 68, 34 (2015)]

## Slide 9
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
ν/νexp (marginal stability)
instability
(NSTX
experiment)
ωφ/ωφexp (marginal stability)
MISK calculations of γτw contours vs. ν and ωφ
Kinetic theory consistent with RWM destabilization at intermediate plasma rotation
Destabilization appears between:
precession resonance at low ωφ
bounce resonance at high ωφ
Precession Drift
~ Plasma Rotation
Rotational resonance effect
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]

## Slide 10: Collisionality affects the strength of kinetic resonances
Collisionality
Collisionality effect
Early theory predicted RWM stability should decrease at low ν
Kinetic RWM stability theory:
  Stabilizing resonant kinetic effects enhanced at low ν
Important for ITER
[J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)]
unstable
(marginal stability)
ν/νexp (marginal stability)
instability
(NSTX
experiment)
ωφ/ωφexp (marginal stability)
MISK calculations of γτw contours vs. ν and ωφ

## Slide 11: Energetic particles provide a stabilizing force that is nearly independent of rotation and collisionality
Energetic particle effect
[J. Berkery et al., Phys. Plasmas 17, 082504 (2010)]
Large for EPs
Small for EPs
Energetic partilces provide stabilizing effect
Energetic particles are not in mode resonance
  Effect is nearly independent of ωφ
  Effect is not energy dissipation, but rather a restoring force
Collisionality
Precession Drift
~ Plasma Rotation
expected ωφ
expected βα
unstable
stable
MISK calculation for ITER

## Slide 12: Outline
RWM Definition and Motivation
Kinetic Stability Theory
  Rotation
  Collisionality
  Energetic Particles
Comparison of Calculations and Experimental Results
Stability Estimation and Rotation Profile Control
Summary

## Slide 13: MISK calculations validated against unstable experimental plasmas; reproduce approach towards marginal stability
MISK calculations including kinetic effects have been tested against many marginally stable NSTX experimental cases
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
unstable
stable
NSTX
NSTX

## Slide 14: Kinetic RWM stability physics unites results from DIII-D and NSTX plasmas
[S. Sabbagh, J. Berkery, J. Hanson, et al., APS invited 2014]
Kinetic RWM stability analysis for experiments (MISK)
major disruption
minor disruption
DIII-D
NSTX
stable
Normalized growth rate (γτw)
Plasma rotation [krad/s] (ΨN = 0.5)
unstable
“weak stability” region
Addition of kinetic effects yields agreement with marginal point in NSTX
Further testing against DIII-D experiments shows good agreement
Strong bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached

## Slide 15: Active MHD spectroscopy experiments show the importance of kinetic effects in stable plasmas as well
[H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)]
DIII-D
[J. Berkery et al., Phys. Plasmas 21, 056112 (2014)]
Favorable rotation range
Resonant field amplification indicates weakening stability
  Plasma response is enhanced where kinetic effects and RWM stability are weak
Discharge trajectories for 20 NSTX plasmas shows favorable ω range
  Matches theoretical expectation for precession drift resonance
NSTX
MISK calculations match experiments

## Slide 16: Outline
RWM Definition and Motivation
Kinetic Stability Theory
  Rotation
  Collisionality
  Energetic Particles
Comparison of Calculations and Experimental Results
Stability Estimation and Rotation Profile Control
Summary

## Slide 17: Physics understanding from previous research used to construct a reduced kinetic model
Real-time velocity data now available on NSTX-U
Goal is to forecast γ in real-time using parameterized reduced models for δW terms
Need δWK as a function of the most important, real-time measurable quantities
Kinetic effects:
Fluid terms
Rotation
Collisionality
+ Energetic Particles
MISK2 Calculations
  Compared to experiments
Reduced Kinetic Model
fluid
kinetic
Rotation controller designed using NBI, NTV

## Slide 18: Summary
RWM stability must be understood for future devices
Kinetic theory modifies ideal stability, includes rotation, collisionality, and energetic particle effects
ITER stability projections show all kinetic effects important
MISK code calculations can explain experimental stability
Reduced models needed for real-time disruption avoidance
Kinetic effects
Fluid terms
~ Rotation
Collisionality
Rotation resonance
Collisionality
Energetic Particles