## Slide 1: Key physics issues and opportunities for next-step spherical torus devices
Jonathan Menard (PPPL)
18th International Congress on Plasma Physics
Kaohsiung Exhibition Center, Kaohsiung, Taiwan
June 27 – July 1, 2016

## Slide 2: Outline
Motivations for studying “spherical” tokamak (ST)
Mission elements of NSTX-U Research Program
NSTX-U research commissioning status
Key physics issues for ST
  Energy transport
  High-beta stability
  Power exhaust
  Current sustainment and start-up

## Slide 3
  High b physics, rotation, shaping extend stability, transport knowledge
  NBI fast-ions in present STs mimic DT fusion product parameters in ITER  study burning plasma science
  STs can more easily study electron scale turbulence at low collisionality  important for all magnetic fusion
ST research extends predictive capability
for ITER and toroidal confinement science
Burning Plasma Physics - ITER

## Slide 4: Recent design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) and Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7, BT=3T
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5, BT = 4T
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)
Designs integrate ST higher k , bN and advanced divertors (+ HTS TF for Pilot Plant)

## Slide 5: Beyond high-BT capability, HTS cables using REBCO tapes achieving very high winding pack current density
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable
Base cable: 50 tapes YBCO Tapes with 38 mm substrate (Van Der Laan, HTS4Fusion, 2015)
Higher Jcable HTS cable concepts under development:
Base Conductor
He Gas Cooled
8kA,
JWP ~ 160MA/m2
7 mm
SS conductor jacket for strength
7 mm
Copper
Conductor on Round Core Cables (CORC)
JWP ~ 70MA/m2 19T

## Slide 6: High current density HTS  more compact TF magnets  lower-A tokamak pilot plants
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
A ~ 2 attractive at high JWP
Pilot: R=3m, PNBI = 50MW, fGW=0.8, fNICD = 1, bN=bN-no-wall (e), k=k(e), H unconstrained, hth = 0.45
JWP [MA/m2]
(12T)
ITER-like TF constraints:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW
  Pnet < -90MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
  Small Pnet at A=2.2-3.5
JWP ≥ 70MA/m2, Bmax ≤ 19T
  Pfusion ~500-600MW
  Pnet = 80-100MW at A=1.9-2.3

## Slide 7: Outline
Motivations for studying “spherical” tokamak (ST)
Mission elements of NSTX-U Research Program
NSTX-U research commissioning status
Key physics issues for ST
  Energy transport
  High-beta stability
  Power exhaust
  Current sustainment and start-up

## Slide 8: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 9: NSTX-U will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 10: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
2017-2018 goals:

## Slide 11: NSTX-U: Operational Research Facility
1st NBI
2nd NBI
NSTX-U
All six NBI sources now operational, supporting high performance experiments

## Slide 12: NSTX-U research initiated January 2016
H-mode access achieved during first 2 weeks of operation

## Slide 13: NSTX-U plasma commissioning status
~9 run weeks of ops, IP = 0.5–1MA, boronized PFCs
Nearly all shots at BT = 0.6-0.65T > NSTX max = 0.55T
All 6 NBI injected into plasmas, 5-10MW routinely available
Approaching NSTX WTOT record ~ 430kJ
NSTX record
Exceeded NSTX L & H-mode pulse-lengths
using 1MW L-modes (0.65, 0.8MA)
NSTX record

## Slide 14: Examples of high-performance L and H-modes achieved thus far in NSTX-U
(motivates cryo-pump)
NEXT: Increase k to avoid tearing, active RWM control, trigger ELMs (DRsep, granule injector)

## Slide 15: Outline
Motivations for studying “spherical” tokamak (ST)
Mission elements of NSTX-U Research Program
NSTX-U research commissioning status
Key physics issues for ST
  Energy transport
  High-beta stability
  Power exhaust
  Current sustainment and start-up

## Slide 16: Favorable confinement trend with collisionality and  found in ST experiments
Promising scaling to ST-FNSF / Pilot, will trend continue on NSTX-U / MAST-U?
ST scaling observed in NSTX and MAST: tE, th µ n*e-0.8 b-0.0
Tokamak empirical scaling (ITER 98y,2): tE, th µ n*e-0.1 b-0.9
Li wall coatings
Boron wall coatings

## Slide 17: NSTX: Global non-linear GTS gyrokinetic simulations have identified multiple low-k turbulence transport mechanisms
Recent GTS simulations have shown possible role of DTEM in contributing to observed favorable collisionality scaling (Bτth~ν*e-0.8)
  In addition to microtearing
  Synergy with DIII-D work
W. Wang et al., NF Letters, PoP (2015)
Energy Flux MW/m2
Strong flow shear can destabilize Kelvin-Helmholtz instability
  Non-linear global GTS simulations
  K-H + ITG + Neo ion transport within factor of 2 of expt’l level
  Cannot account for electron transport
Ions
Electrons

## Slide 18: NSTX: Large inferred anomalous core electron transport in presence of CAE/GAEs
Observation of high frequency Compressional/Global Alfven Eigenmodes (CAE/GAE) modes in plasma core associated with flattening of Te profile (Stutman, Tritz - JHU)
  High level of transport (10-100 m2/s) inferred assuming classical beam physics
BES spectra show mode amplitudes peaking from R=115 to 120 cm (r/a~0.2 to 0.3), in region of enhanced transport
Stutman
Smith
CAE/GAE
Is enhanced transport the full picture?
~dn amplitude of 738 kHZ CAE/GAE

## Slide 19: New NSTX-U result: suppression of counter-propagating GAE observed for large RTAN 2nd NBI
Top panel: GAE excited by inboard sources 1B / 1C
Injection of new outboard source 2B starts at 0.192s  suppression of GAE
  Suppression also with 2A, 2C
Observations consistent with model of cyclotron-resonant drive of GAE
Will investigate whether GAE absence impacts electron thermal transport
 2nd NBI already powerful new tool for Fast Ion and AE physics

## Slide 20: New 2nd NBI: L-mode core sawtooth and tearing dynamics change with source tangency radius
Most
on-axis
2nd NBI
Most
tangential
2nd NBI

## Slide 21: Outline
Motivations for studying “spherical” tokamak (ST)
Mission elements of NSTX-U Research Program
NSTX-U research commissioning status
Key physics issues for ST
  Energy transport
  High-beta stability
  Power exhaust
  Current sustainment and start-up

## Slide 22: Dedicated tokamak + ST experiments found power exhaust width varies as 1 / Bpoloidal
ST data breaks aspect ratio degeneracy of data set
Will 1/Bpoloidal variation continue at higher IP? What about detached conditions?

## Slide 23: MAST-U and NSTX-U will test radiation and advanced divertors for mitigating high heat-fluxes
MAST-U: Conventional (CD), Snowflake (SFD), Super-X (SXD)
NSTX-U: Snowflake (SFD) / X-D
R [m]
Z [m]
Assess impact of flux expansion, line length on detachment
Longer-term:
  C PFCs Liquid Li on high-Z substrates

## Slide 24: Outline
Motivations for studying “spherical” tokamak (ST)
Mission elements of NSTX-U Research Program
NSTX-U research commissioning status
Key physics issues for ST
  Energy transport
  High-beta stability
  Power exhaust
  Current sustainment and start-up

## Slide 25: Steady-state operation required for ST/AT FNSF or Pilot Plant
NSTX achieved 70% “transformer-less” current drive
NSTX-U designed to achieve 100% (TRANSP):
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier
Will NSTX-U achieve 100% as predicted by simulations?

## Slide 26: ST-FNSF may need solenoidless current start-up method Coaxial Helicity Injection (CHI) effective for current initiation
CHI developed on HIT, HIT-II
Transferred to NSTX / NSTX-U
NSTX: 150-200kA closed flux current
R. Raman et al., PRL 2006
NSTX-U: CHI projects to 300-400kA
FNSF: CHI blanket electrodes: 2MA
2
2
2
R (m)
R (m)
0
Z (m)
1.0 ms 1.6 ms 2.7 ms
R (m)
0
0
2
0
-2
What about 3D effects?
TSC axisymmetric simulation of CHI startup

## Slide 27: NIMROD simulations: plasmoid-mediated reconnection assists flux closure at high Lundquist number
Sweet Parker (S-P) reconnection in the injector region at low Lundquist number
At high Lundquist number the S-P current sheet is plasmoid unstable
Plasmoids seen in modelling before found/observed in CHI data!
F. Ebrahimi, et al., PRL (2015)
P
l
a
s
m
o
i
d
s
S
i
m
u
l
atio
o
n
E
x
p
e
r
i
m
e
n
t

## Slide 28: Summary: ST research making leading contributions to fusion energy development
Support burning plasma research by expanding understanding of energetic particle, thermal transport
Will explore performance and implications of advanced divertor configurations, liquid metals
ST promising as Fusion Nuclear Science Facility
  High JWP of HTS  enables compact lower-A Pilot Plant
NSTX-U operational now!
MAST-U first plasma next year!

## Slide 29: See more ST-related talks this week

## Slide 30: Backup Slides - Physics

## Slide 31: Optimal n=1 error field correction amplitude and phase identified to maximize pulse length, discharge performance
Dominant error-field source: PF5 vertical field coils
Long-pulse L-modes used to identify optimal correction amplitude, phase

## Slide 32: On path to high IP without tearing modes by elevating qmin with early heating + H-mode  li=0.5-0.6, k=2.5-2.7
Matching NSTX k at same li but at higher A
  Real-time EFIT / ISOFLUX (GA collaboration)
  Also utilizing improved vertical motion detection

## Slide 33: NSTX-Theory collaborations have led the advancement in kinetic global mode stability physics
MARS-K: Ideal wall stability (Menard)
MARS-K: Resonant field amp. (Wang)
RWM High-beta stability physics theory
MISK: RWM High-beta stability (Berkery, Sabbagh)
Experiment
(Betti, Berkery,
Sabbagh)
Precession drift
resonance stabilization
Bounce/transit
resonance stabilization
Marginal stability
instability
(experiment)
RWM physics with M3D-C1 (Ferraro)
Resistive wall implemented

## Slide 34: NBI-heated STs excellent testbed for -particle physics
-particles couple to Alfvénic modes when V > VAlfvén~ -0.5 Csound
Vfast > VA condition easily satisfied in high-b ST with NBI heating
NSTX-U: large fast-ion dynamic range spanning ST and conventional A
  Toroidal field 2× NSTX  Vfast < VA  stabilize modes
  Tangential 2nd NBI  very flexible fast-ion distribution
    Vary pitch angle, pressure profile
Can we find TAE-quiescent, high-performance regimes in NSTX-U?

## Slide 35: “TAE avalanche” can cause energetic particle loss Uncontrolled -particle loss could cause reactor first wall damage
Quasi-linear “Critical Gradient Model” (CGM) consistent with transport before avalanche
“Kick” model (DPf vs DE) predicts neutron decrement even during large avalanche events
NSTX 141711
Time [ms]
Neutron Deficit %

## Slide 36: NSTX-U NIMROD projection: high fraction of open flux converted to closed flux with narrow injector flux footprint
CHI in NSTX-U configuration naturally has a narrower injector flux foot-print due to improved Injector coil positioning
Due to higher Lundquist number in NSTX-U CHI simulations, closed flux surfaces form even during the actively injected phase
F. Ebrahimi, et al., accepted in NF Letters
NIMROD Simulations

## Slide 37: Plasma confinement increased continuously with increasing Li coatings in NSTX – what is limit?
Global parameters improve
  H98y2 increases ~0.9  1.4
  No core Li accumulation
High H critical for compact FNSF / Pilot Plants
NSTX-U will double Li-wall coverage with upward evaporators
Will further assess contributors to confinement improvement:
  Lower-recycling / reduced neutral source / higher Te
  Edge profile / turbulence changes
  Influence of (low-Z) impurities in pedestal region
Energy Confinement Time (ms)
Pre-discharge lithium evaporation (mg)
R. Maingi, et al., PRL 107 (2011) 145004

## Slide 38: NSTX-U boundary / PFC plan: add divertor cryo-pump, transition to high-Z wall, study flowing liquid metal PFCs
5yr goal: Integrate high E and T with 100% non-inductive
10yr goal: Assess compatibility with high-Z & liquid lithium PFCs
Cryo + full lower outboard high-Z divertor
Lower OBD
high-Z row of tiles
B+C BN
Li High-Z
2016
2017-18
2018-19
Heatable high-Z PFCs for liquid Li (including pre-filled)
Cryo + high-Z FW
and OBD
+ liquid Li divertor (LLD)
2020-21
High-Z tile row
Up + downward Li evaporator, possible pre-filled Li tiles (FY18)
High-Z tile row
All high-Z FW +
divertors
+ flowing LLD
module
2022-23
or
Flowing Li module (Concept, location, size TBD)
Cryo-pump
Downward Li evaporator +
Li granule injector
See Maingi, Jaworski talks for more details

## Slide 39: Backup Slides – Cu TF FNSF

## Slide 40: Identified self-consistent configuration for power exhaust, equilibrium flexibility, breeding, maintenance
2nd X-point increases SOL line-length
Breeding at top/bottom important for maximizing TBR
PF coil set supports wide range of li: 0.4-0.8
  Elongation and squareness change with li variation
  Fixed strike-point R, controllable B angle of incidence (0.5-5˚)
Divertor coils in TF coil ends for equilibrium, high d
Increased strike-point radius reduces B, q||
Strike-point PFCs also shielded by blankets
TF coil
All equilibrium PF coils outside vacuum vessel
PF coil
Blanket
Vessel
Components:
k = 2.55, li = 0.82
k = 3.0, li = 0.40
Shield
No central solenoid in this design

## Slide 41: Long-leg divertor reduces heat flux 3×to ~10MW/m2 Also promotes detachment  additional 5-10×reduction
lq-int = 2mm, 4mm
Peak q < 10MW/m2
SOLPS
J. Canik

## Slide 42: Used free-boundary TRANSP/NUBEAM to specify NBI and simulate 100% non-inductive plasmas with QDT ~2
Neoclassical cion
ne / nGreenwald = 0.7
H98,y2 = 1.4
IP = 8.9MA, BT = 2.9T
fNICD = 100%, fBS = 65%
PNNBI = 80MW (0.5MeV)
Pfus = 200MW (50-50 DT)
  2.6% alpha bad orbit loss
QDT = 2.5
bN = 5.5, Wtot = 58MJ
  Wfast / Wtot = 14%
Maintain qmin > 2, q(0) / qmin controllable via Rtan and density

## Slide 43
Developed detailed CAD models for 2 different sizes
(R = 1m and 1.7m – most analysis done for R=1.7m configuration)
Cu/SC PF coils housed in VV lower shell structure
SC PF coils pairs located in common cryostat
TF leads
Vertical maintenance
Design features
Cu/SC PF coils housed in VV upper lid
VV outer shell w/ shield material
Angled DCLL concentric lines to external header
Ports for TBM, MTM, NBI
Blankets
TF coils

## Slide 44: Conformal blankets + breeding at top/bottom important for tritium breeding ratio TBR ~ 1
Inner Blanket Segment = 0.81
Outer Blanket Segment = 0.15
Total TBR ~ 1.03 with no penetrations or ports
(heterogenous outboard blanket)
0.0004
0.0004
0.034
0.034
DTBR = +0.07
R=1.7m configuration

## Slide 45: Quantified impact of TBM, MTM, NBI ports on TBR
No ports or penetrations,
homogeneous breeding zones:
TBR = 1.03
Add 4 Test Blanket
Modules (TBMs)
TBR = 1.02 (DTBR = -0.01)
TBM
LiPb,
cooling channel,
FCI
1 Materials Test Module (MTM)
TBR = 1.01 (DTBR = -0.02)
Ferritic Steel
MTM
4 TBM + 1 MTM + 4 NBI
TBR = 0.97
Approx. DTBR per port:
TBM: -0.25%
MTM: -2.0%
NBI: -0.75%

## Slide 46: Find R ≥ 1.7m necessary for TBR ≥ 1 at A=1.7
R=1.7m: TBR ≥ 1
R=1.0m: TBR < 1 (≈ 0.9)
TBM
NBI
MTM
TBM
MTM
NBI
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 47: FNSF center-stack can build upon NSTX-U design and incorporate NSTX stability results
Like NSTX-U, use TF wedge segments (but brazed/pressed-fit together)
  Coolant paths: gun-drilled holes or grooves in side of wedges + welded tube
Bitter-plate divertor PF magnets in ends of TF achieve high triangularity
  NSTX data: High d > 0.55 and shaping S  q95IP/aBT > 25 minimizes disruptivity
  Neutronics: MgO insulation can withstand lifetime (6 FPY) radiation dose

## Slide 48
Glidcop plates
Insulator
Bitter coil insert for divertor coils in ends of TF

## Slide 49: MgO insulation appears to have good radiation resistance for divertor PF coils

## Slide 50
VV lid / PF cryostat enclosure
Full blanket assembly
TF center-stack
Upper TF horizontal legs
Upper dome structure located on test cell shield plug
TF power supplies
JT-60SA NNBI
R=1.7m ST-FNS facility layout
using an extended ITER building

## Slide 51: Backup Slides – HTS TF FNSF

## Slide 52: What is optimal A for HTS FNSF / Pilot Plant?
Pfus / V ~ e(bN k BT )4 at fixed bootstrap fraction
bN and k increase at lower aspect ratio
BT decreases at lower A – depends strongly on:
  Inboard shielding, HTS allowable field and current density
Approach:
Fix plasma major radius and heating power (50MW)
  R0 = 3m – smallest size for Qeng > 1 and high fluence
Apply magnet & plasma constraints (see backup)
  HTS strain: 0.3%, bN: n=1 no-wall, k: 0.95×limit, fGW = 0.8
Vary aspect ratio from A = 1.6 to 4
Vary HTS current density, peak field
  Also scan inboard shielding thickness (not shown)
Compute QDT, Qeng, and required H98 (unconstrained)

## Slide 53: Engineering constraints
Magnet constraints
  Maximum stress in TF magnet structure = 0.66 GPa
  HTS tape/cable strain limit 0.3% (equivalent to 0.4 GPa)
  Winding pack current density (CORC 2015) 70 MA/m2
  OH at small R  higher solenoid flux swing for higher A
Shielding / blankets
  HTS fluence limit: 3.5x1022 n/m2
  Shield:10x n-shielding factor per 15-16cm WC for HTS TF
  Include inboard & outboard breeder thickness for TBR ~ 1
    “Effective shield thickness” includes shield + DCLL blanket
Electrical system efficiency assumptions:
  30% wall plug efficiency for H&CD - typical of NNBI
  ≥ 45% thermal conversion efficiency - typical of DCLL
    Also include pumping, controls, other sub-systems
    See Pilot Plant NF 2011 paper for more details

## Slide 54: Aspect ratio dependence of limits: k(e), bN(e)
NSTX data at low-A
  Also NSTX-U/ST-FNSF modelling
DIII-D, ARIES-AT for higher A
  k  1.9 for A  
Profile-optimized no-wall stability limit at fBS ≈ 50%
  Menard PoP 2004
bN  3.1 for A  
bT  A-1/2 (1+k2) bN2 / fBS
 Pfus  e [k(e) bN(e) BT(e)]4
e = A-1
Pilot study uses 0.95×k value shown here:

## Slide 55: Simplified TF magnet design equations
From J. Schwartz, Journal of Fusion Energy, Vol. 11, No. 1, 1992

## Slide 56
A=2, R0 = 3m device TF inboard leg showing
allocated space for case and winding
0.167 m2 winding area
Current per coil: 6 MA
Winding Cd: 35.9 MA/m2

## Slide 57
CORC Conductor – Achieved now
10 mm
10 mm
6 mm
857 turns @ 7 kA
(848 turns shown; a few additional turns required)
Base Conductor – Helium Gas Cooled
7 mm
SS conductor jacket for strength
7 mm
Copper
750 turns @ 8 kA
(750 turns shown)

## Slide 58: HTS performance vs. field and fast neutron fluence

## Slide 59: Neutronics analysis for HTS TF shielding

## Slide 60: Breeding blanket thickness model

## Slide 61: High TF winding-pack current density required to access highest BT at lower A
12T: ITER-like TF coil limit
(Nb3Sn, 11.8T)
19T: Present CORC HTS limit
JWP [MA/m2]
Chart: Max BT at TF coil [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 18.3214 | 18.7622 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
80 | 16.433 | 17.1602 | 17.7576 | 18.1294 | 18.4409 | 18.7044 | 18.9935 | 18.9996 | 18.9999 | 19 | 19 | 19
40 | 11.266 | 13.8912 | 16.0357 | 16.4935 | 16.8683 | 17.1797 | 17.6277 | 18.277 | 18.8214 | 19 | 19 | 19
30 | 8.4495 | 10.4184 | 12.1777 | 13.3057 | 14.277 | 15.1135 | 16.3799 | 17.2829 | 17.8659 | 18.3192 | 18.9755 | 19
20 | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12.2231 | 13.3857 | 14.3299 | 15.7496 | 16.7393
20 (12T) | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12 | 12 | 12 | 12 | 12
Chart: BT at geometric center [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 2.1314 | 2.8724 | 3.5298 | 3.927 | 4.2687 | 4.5627 | 5.0076 | 5.6937 | 6.3054 | 6.802 | 7.5484 | 8.0687
70 | 1.9117 | 2.6272 | 3.299 | 3.7471 | 4.1431 | 4.4917 | 5.0059 | 5.6935 | 6.3054 | 6.802 | 7.5484 | 8.0687
40 | 1.3106 | 2.1267 | 2.9791 | 3.4089 | 3.7897 | 4.1256 | 4.6459 | 5.477 | 6.2462 | 6.802 | 7.5484 | 8.0687
30 | 0.98296 | 1.595 | 2.2623 | 2.7501 | 3.2076 | 3.6294 | 4.317 | 5.1791 | 5.929 | 6.5583 | 7.5387 | 8.0687
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.6629 | 4.4422 | 5.1301 | 6.2571 | 7.1086
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.596 | 3.9824 | 4.296 | 4.7674 | 5.096
Coil structure sized to maintain ≤ 0.3% strain on winding pack for all cases shown here

## Slide 62: A ≥ 2 pilot plant scenarios have elevated H > 1, fBS ~ 80%, IP = 6-12MA
JWP [MA/m2]

## Slide 63: A=2, R0 = 3m HTS-TF FNSF / Pilot Plant
Cryostat volume ~ 1/3 of ITER
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%
H98 = 1.8, HPetty-08 = 1.3
fgw = 0.80, fBS = 0.76
Startup IP (OH) ~ 2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW, ENBI = 0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence = 7 MWy/m2

## Slide 64: Breeding calculations nearly complete for A=2
Outboard TBR ~ 0.92
Ongoing: Thin inboard blanket (10 cm) should provide TBR > 1
Step 1- Infinite media of LiPb
Step 2- LiPb confined to OB FW/blanket
Step 3- Assembly gaps added
Step 4- Homogeneous mixture of blanket in upper and lower ends of OB blanket
Step 5- FW material added
Step 6- Side, back, and front walls added
Step 7- Cooling channels added
Step 8- SiC FCI added
Step 9- Stabilizing shells added
Step 10- MTM only inserted (TBR relative to Step #9)
Step 11- 4 TBMs only inserted (TBR relative to Step #9)
Step 12- 4 NBIs only inserted (TBR relative to Step #9)
Step 13- all MTM, 4 TBMs, and 4 NBIs inserted
Step 14 – include inboard breeding blanket

## Slide 65: Exploring liquid metal divertor design similar to flowing water curtain systems
Ferritic steel backing plate
Shield block
LM containment structure
LM injector system can be assembled in a single or double unit

## Slide 66: HTS ST-FNSF design with Li flow on divertor and inboard surfaces
Double null liquid metal divertor system
Li flows from upper divertor down the inboard wall, exiting just after the lower inboard divertor.
Separate Li cooling of lower divertor

## Slide 67: Another option: Li divertor with shorter outer leg Pdiv = 9  21MW/m2 for Rstrike = 4.2m  2.5m
Long-leg / Super-X
Shorter leg LM divertor
Geometry also compatible with
“vapor box” concepts (Ono / Goldston)

## Slide 68: Benefits of shorter-leg LM high-heat-flux divertor:
Significantly reduce outboard PF coil current
  Reduced PF size, force, structure
Eliminate separate upper cryo-stat (for PF5U)
1
2
3
4
5
6
7
8
Li wall pumping could help increase H (see Maingi talk)