## Slide 1
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
NSTX-U
Supported by
Resistive Wall Mode Stability in NSTX and Benchmarked Kinetic Physics Calculations with MISK
18th Workshop on MHD Stability Control
Santa Fe, NM
November 18, 2013
J.W. Berkery1, S.A. Sabbagh1, A. Balbaky1, R.E. Bell2,
R. Betti3, J.M. Bialek1, A. Diallo2, D.A. Gates2, S.P. Gerhardt2,
B.P. LeBlanc2, Y.Q. Liu4, N.C. Logan2, J. Manickam2, J.E. Menard2, J.-K. Park2, M. Podestà2, Z.R. Wang2, H. Yuh5
1Columbia U., 2PPPL, 3U. Rochester, 4CCFE, 5Nova Photonics

## Slide 2: The highest performance plasmas are not the least stable in NSTX Kinetic stabilization can explain this favorable result
Outline:
Measured stability in experiments using active MHD spectroscopy
  Stability vs. βN/li
  Stability vs. collisionality
  Stability vs. rotation
MISK kinetic RWM stabilization code analysis
  MISK / MARS-K / PENT benchmarking
  Application of MISK to the above experiments

## Slide 3: An unstable RWM is an exponential growth of magnetic field line kinking that can be studied with a linear model
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Linear, perturbative model is justified
Bp
RWMs in NSTX cause a collapse in β, disruption, and termination of the plasma

## Slide 4: NSTX reaches high βN, low li range of next-step STs and the highest βN/li is not the least stable
0
li
0.0
0.2
0.4
0.6
bN
li
bN/li
13
12
11
14
[S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)]
[S. Gerhardt et al., Nucl. Fusion 53, 043020 (2013)]
8
6
4
2
0
bN
8
6
4
0.0
0.2
0.6
0.8
0.8
bN/li
13
12
11
14
10
10
0.4
NSTX can reach high β, low li range where next-step STs aim to operate
The highest βN/li is not the least stable in NSTX
  In the overall database of NSTX disruptions, disruptivity deceases as βN/li increases
  Active control experiments reduced disruption probability from 48% to 14%, but mostly in high βN/li
Unstable RWM
Stable/Controlled RWM
βN/li = 6.7 : computed
NSTX n = 1 no-wall limit
2

## Slide 5: High beta plasma stability is directly measured to test experimental trend of disruptivity
Active MHD spectroscopy is used to measure RWM stability when modes are stable
  Resonant field amplification of n=1 applied AC field is measured
  Increased RFA indicates decreased stability
[H. Reimerdes et al., Phys. Rev. Lett. 93, 135002 (2004)]
40 Hz n=1 tracer field
n=3 braking
Resonant field amplification (RFA)
RFA = Bplasma/Bapplied

## Slide 6: Dedicated NSTX experiments reveal stability dependencies that can not be explained by early theories
A series of 20 discharges was generated in NSTX
  Trajectories of RFA amplitude vs. key parameters for this database shows the stability space
How can we explain this behavior?
Compare theory expectations to experimental results
Use the full kinetic calculation of the MISK code for greater insight
Stability increases at the highest βN/li
Stability is weakest, and unstable plasmas are found, at intermediate βN/li

## Slide 7: Collisionality affects the strength of kinetic resonances, experimental results consistent with theoretical expectation
MISK calculations
0.2
1.2
1.4
1.3
1.5
0.4
0.6
0.8
1.0
Precession Drift
~ Plasma Rotation
Collisionality
unstable
stable
on-resonance
more stable
 ~ -1/ν
off-resonance
less stable
 ~ constant
Early theory predicted RWM stability to decrease at low ν
Kinetic RWM stability theory at low ν:
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)

## Slide 8: The stability boundary vs. ExB frequency can be explained by kinetic resonances, favorable range found
Average range
Pedestal
Precession Drift
~ Plasma Rotation
ExB frequency radial profile
Evaluate <ωE> inside the pedestal
  Quantity can be evaluated in future real-time systems
  Favorable range, <ωE> ≈ 4-5 kHz, found experimentally

## Slide 9: Stability boundaries in NSTX from MHD spectroscopy are explained by kinetic theory, have favorable dependencies
Discharge trajectories for 20 plasmas
a) Stability vs. βN/li
Stability increases at
the highest βN/li due to kinetic effects
b) Stability vs. collisionality
Stable plasmas appear to benefit further from reduced collisionality
c) Stability vs. rotation
Precession drift resonance is stabilizing, useful for disruption avoidance

## Slide 10: Kinetic effects arise from the perturbed pressure, are calculated in MISK from the perturbed distribution function
Force balance:
leads to an energy balance:
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved for in the MISK code by using from the drift kinetic equation to solve for
Precession Drift
~ Plasma Rotation
Collisionality

## Slide 11: Benchmarking of codes calculating RWM stability was carried out under the ITPA, MDC-2
Calculations of RWM stability with kinetic effects were performed
  with MISK, MARS-K (perturbative), and PENT (interfaces with IPEC)
  without collisions or energetic particles
  for the three cases shown below
Solov’ev 1:
near circular, no rationals
Solov’ev 3:
shaped, q = 2 and 3
ITER:
no alphas, no collisions

## Slide 12: Benchmarking of codes calculating RWM stability was carried out under the ITPA, MDC-2
Calculations of RWM stability with kinetic effects were performed
  with MISK, MARS-K (perturbative), and PENT (interfaces with IPEC)
  without collisions or energetic particles
  for the three cases shown below
Solov’ev 1:
near circular, no rationals
Frequencies,
Energy integrals,
Eigenfunctions,
Lagrangian terms,
δWK profile vs. ψ,
δWK vs. ωE
τw vs. ωE

## Slide 13: Initial comparison showed disagreement, especially for the ITER case
 | Ideal dW/-dW¥ | Re(dWk) /dW¥ | Im(dWk)/ (dW¥) | gtwall | wtwall
Solov’ev 1 (MARS-K) (MISK) | 1.187 1.122 | 0.0256 0.0243 | -0.0121 0.0280 | 0.804 0.850 | -0.0180 -0.0452
Solov’ev 3 (MARS-K) (MISK) | 1.830 2.337 | 0.208 0.371 | -0.343 0.0601 | 0.350 0.232 | -0.228 -0.0273
ITER (MARS-K) (MISK) | 0.682 0.677 | 141.5 0.665 | 2.286 -0.548 | -0.988 0.0709 | 0.00019 0.437
Originally MISK was more consistent with MARS-K self consistent
  MARS-K perturbative numbers very large for ITER

## Slide 14: Agreement now found between MISK and MARS-K for all cases considered under MDC-2 Benchmarking
 | Ideal dW/-dW¥ | Re(dWk) /dW¥ | Im(dWk)/ (dW¥) | gtwall | wtwall
Solov’ev 1 (MARS-K) (MISK) | 1.187 1.122 | 0.0218 0.0208 | -0.0121 -0.0068 | 0.803 0.861 | 0.0180 0.0189
Solov’ev 3 (MARS-K) (MISK) | 1.830 2.337 | 0.0794 0.0892 | -0.147 -0.090 | 0.471 0.374 | 0.114 0.051
ITER (MARS-K) (MISK) | 0.682 0.677 | 0.241 0.367 | -0.046 -0.133 | 0.817 0.581 | 0.090 0.202
Improvements were made to both codes
  MISK corrected ωD calculation, some minor input changes
  MARS-K correction of error in particle phase factor in bounce resonance

## Slide 15
δWK vs radius for ITER case – points to key difference
Example: d(dWk)/dψ vs. ψ shows good agreement between codes
  Except at the plasma edge (work continues)
  Except very close to rational surfaces
Agreement found between MISK and MARS-K when integration is not taken very close to the rationals
Precession resonant ions
Bounce resonant ions

## Slide 16: Benchmarking of RWM stability codes through the ITPA was successful; codes agree and support present understanding
fluid growth rates
fluid plus kinetic growth rates
unstable
stable
low rotation
precession
resonance
high rotation
bounce/transit
resonance
The codes support the present understanding that RWM stability can be increased by kinetic effects
  At low rotation through precession drift resonance
  At high rotation by bounce and transit resonances
  Intermediate rotation can remain susceptible to instability
The successful benchmarking gives great confidence that these codes are correctly calculating kinetic effects of RWM stability
  To the extent that this model is validated against experimental evidence of RWM stability, one can then project the stability of future devices with greater confidence
ITER case
[J. Berkery et al., “Benchmarking Kinetic Calculations of Resistive Wall Mode Stability”, Report to the ITPA (2013)]

## Slide 17: MISK calculations of precession drift resonance of many equilibria are consistent with the measured βN/li trend
MISK code calculation for 44 equilibria from the 20 discharge database
Less stable
δWK small
More stable
δWK large
Precession Drift
~ Plasma Rotation
bounce harmonic l = 0
MISK calculations

## Slide 18: Experimental stability trends in NSTX can be explained by kinetic theory, which benchmarked MISK can calculate
For the first time it has been found in NSTX that disruption probability decreases at the highest βN/li
Kinetic stability of resistive wall modes can explain this new and highly-favorable result
  Whereas past theory showed low ν to be destabilizing, here stable plasmas appear to benefit further from reduced collisionality (good for future devices)
  Stabilizing precession resonance is useful for disruption avoidance
Benchmarking of RWM stability codes successfully completed
  The codes agree and support present understanding of rotation resonance stabilization

## Slide 19: backup slides

## Slide 20: MISK calculations of kinetic RWM growth rate for individual equilibria compares well with marginal stability point
MISK calculations with scaled experimental rotation profiles show:
  Stable discharges calculated as stable
  Marginally stable discharge predicted unstable with 20% reduction in rotation
MISK calculations

## Slide 21: NSTX is a spherical torus equipped to study passive and active global MHD control, rotation variation by 3D fields
RWM active stabilization coils
RWM poloidal sensors (Bp)
RWM radial sensors (Br)
Stabilizer
plates
High beta, low aspect ratio
  R = 0.86 m, A > 1.27
  Ip < 1.5 MA, Bt = 5.5 kG
  βt < 40%, βN > 7
Copper stabilizer plates for kink mode stabilization
Midplane control coils
  n = 1 – 3 field correction, magnetic braking of ωφ by NTV
  n = 1 RWM control
Combined sensor sets now used for RWM feedback
  48 upper/lower Bp, Br
NBI port hole

## Slide 22: Kinetic effects in the RWM dispersion relation allows for passive stabilization of the RWM, can explain experiments
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink Mode
Resistive Wall Mode
Resistive Wall Mode (RWM) fluid dispersion relation:
τw-1 is slow enough that active stabilization (feedback) can keep the plasma stable
Kinetic Effects
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]

However, NSTX experiments have often operated in this range without active control!
Passive stabilization
  Collisional dissipation
  Rotational stabilization
    Simple models with a scalar “critical rotation” level for stability could not explain experiments
[S. Sabbagh et al., Nucl. Fusion 50, 025020 (2010)]
~τw-1
with kinetic effects?

## Slide 23: NSTX reaches high βN, low li range of next-step STs and the highest βN/li is not the least stable
bN
li
bN/li
13
12
11
10
14
ST-CTF
ST-Pilot
Next-step STs aim to operate at:
  High βN for fusion performance
  High non-inductive fraction for continuous operation
    High bootstrap current fraction -> Broad current profile -> Low internal inductance, li = <Bp2>/<Bp>ψ2
This is generally unfavorable for ideal global MHD mode stability
  Low li reduces the ideal n = 1 no-wall beta limit
[S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)]
8
6
4
2
0
0.0
0.2
0.6
0.8
0.4
NSTX can reach high β, low li range where next-step STs aim to operate
Recent years with n = 1 RWM feedback in red
βN/li = 6.7 : computed
NSTX n = 1 no-wall limit

## Slide 24: A comparison example: frequency, and energy integral calculations match between codes
Both numerical and analytical approaches
IPEC PENT being developed: good agreement as well
Energy
integral
Bounce frequency vs. pitch angle
Re(energy integral) vs. pitch angle

## Slide 25: Eigenfunction quantities generally in good agreement between MARS-K and MISK
Re(Ñ·x^) contours
(MARS-K)
Re(Ñ·x^) contours
(MISK)
Solov’ev 3 case

## Slide 26: Eigenfunction quantities in very good agreement in core, with some differences in the edge region
Re(Ñ·x^) vs. poloidal angle
(yn = 0.9)
Re(Ñ·x^) vs. poloidal angle
(yn = 0.585)

## Slide 27: Dedicated NSTX experiments reveal stability dependencies that can not be explained by early theories
Experiments in NSTX measured RFA of high beta plasmas with rotation slowed by n=3 magnetic braking
  Blue: unstable at 0.9 s
  Green: higher β, lower rotation: stable
  Counter-intuitive without invoking kinetic effects

## Slide 28
precession resonant ions and electrons
bounce and transit resonant ions
MISK, MARS-K, and PENT agree in δWK vs ωE for ITER

## Slide 29: Collisionality affects the strength of kinetic resonances, experimental results consistent with theoretical expectation
Early theory predicted RWM stability to decrease at low ν
Kinetic RWM stability theory at low ν:
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
MISK calculations
0.2
1.2
1.4
1.3
1.5
0.4
0.6
0.8
1.0
on-resonance
more stable
 ~ -1/ν
off-resonance
less stable
 ~ constant
[J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)]
unstable
stable
Precession Drift
~ Plasma Rotation
Collisionality

## Slide 30: Collisionality affects the strength of kinetic resonances, experimental results consistent with theoretical expectation
MISK calculations
0.2
1.2
1.4
1.3
1.5
0.4
0.6
0.8
1.0
Precession Drift
~ Plasma Rotation
Collisionality
unstable
stable
on-resonance
more stable
 ~ -1/ν
off-resonance
less stable
 ~ constant
Early theory predicted RWM stability to decrease at low ν
Kinetic RWM stability theory at low ν:
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
Expectations for lower ν tokamaks (ITER):
  Stronger stabilization near resonances
  Almost no effect off-resonance

## Slide 31: The stability boundary vs. ExB frequency can be explained by kinetic resonances, favorable range found
low rotation
less stable RWMs
intermediate rotation
less
stable RWMs
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
Average range
Pedestal
Precession Drift
~ Plasma Rotation
ExB frequency radial profile
precession drift
resonance stabilization
Evaluate <ωE> inside the pedestal
  Quantity can be evaluated in future real-time systems

## Slide 32: The stability boundary vs. ExB frequency can be explained by kinetic resonances, favorable range found
Average range
Pedestal
Precession Drift
~ Plasma Rotation
ExB frequency radial profile
Evaluate <ωE> inside the pedestal
  Quantity can be evaluated in future real-time systems
  Favorable range, <ωE> ≈ 4-5 kHz, found experimentally