## Slide 1: PPPL ST-FNSF Engineering Design Details
Tom Brown
TOFE Conference
November 10, 2014

## Slide 2
Some suggest to move from ITER by constructing a prototypical demonstration device (DEMO) that precedes a power plant; others
Define a smaller scale “Pilot Plant” that generates net electricity Qeng ≥ 1 as quickly as possible before building DEMO and
Some suggest that prior to building a DEMO device or Pilot Plant, it would be best to first operate a smaller Fusion Nuclear Science Facility (FNSF) to develop the blanket technology used for thermal power conversion and tritium breeding.
A number of roadmaps have been prescribed that lead to a fusion power plant from ITER
Fusion Roadmaps

## Slide 3
ST-FNSF Study Objectives
Provide a fusion-relevant neutron wall loading (1MW/m2) and neutron fluence of 6MW-yr/m2 to develop and test fusion blankets
Obtain a better understanding of the copper ST option in sizing a device to achieve a tritium breeding ratio TBR ≥ 1
Understand the opportunities offered by a smaller (TBR < 1) device
Review the engineering details in developing the ST approach for FNSF balancing physics requirements and engineering constraints within a developed configuration arrangement that is amenable to in-vessel component maintenance.
Broader mission requirements for FNSF will impact design options and the selection process

## Slide 4
ITER
Device parameters: 4m, 6T B0
Double-null divertor
Qengr ≥ 1
Steady-state
T self-sufficient with TBR ≥1
DEMO blankets and divertors
Power plant prototyped RM
AT-Pilot Plant
S/C magnets
ST-FNSF
Device size: 1 - 1.7m,
Double-null divertor
Steady-state
TBR: 0.88 to 1
DEMO blankets and divertors
K-DEMO
Fusion Roadmap options

## Slide 5
Significant progress has been made in ST-FNSF Studies
Ex-vessel PF coils have been arranged to form a Super-X /snowflake divertor that operate with low heat loads,
A credible vertical maintenance scheme was developed to gain access to internal blanket modules, and
Port cut-outs were defined to support NNBI yet left sufficient blanket material to generate high TBR values.
Progress made

## Slide 6
TF horizontal legs
Magnet system upper beam structure
Blanket system
VV lid with S/C PF coils embedded in local cryostat
TF center post
PPPL 1.7-m ST-FNSF Device
Section Isometric view
Exploded view

## Slide 7
Field on axis: 3T
Double-null divertor
<Wn>: 1 MW/m2
Pfus: 116 MW
Steady-state
TBR ~1
DEMO blankets and divertors
Paux: 80 MW
ST-FNSF Device Size
Field on axis: 3T
Double-null divertor
<Wn>: 1 MW/m2
Pfus : 62 MW
Steady-state
TBR 0.88
DEMO blankets and divertors
Paux: 60 MW

## Slide 8
In-vessel details
MgO Cu Bitter plate PF pair located within TF center post
PF arrangement defines a Super-X/snowflake divertor
Double wall VV structure that contains tungsten carbide (WC) balls and borated water
External S/C PF coils contained in local cryostat
Plasma contoured outboard breeding blanket with local blanket above (below) divertor
Shielding sufficient to meet operation at 6 FPY
MgO Cu Bitter plate PF coils

## Slide 9
Reduced divertor heat load
The projected Super-X/snowflake divertor peak heat flux can be reduced by up to a factor of 3 relative to a conventional divertor to ≤ 10MW/m2 even for nominally attached conditions for surface-average neutron wall loading Wn = 1MW/m2.
The ability to operate with a Super-X/snowflake divertor places higher requirements on the PF system – more coils operating at higher currents, for coils located a distance from the plasma.

## Slide 10
TF center post details

## Slide 11
Impact of solenoid free start-up
Design features were added to a DCLL blanket segment to support the requirements of a coaxial Helicity injection (CHI) start-up scenario

## Slide 12
NNBI / facility layout
Four angled beams were placed in the 1.7m device (three for the 1m) with tangency values ranging from R0, R0+a/2 to R0+.75a
The ITER building was used in sizing the test cell for the 1.7m case, resulting in a building of similar length but somewhat reduced width and height

## Slide 13
TF power supplies
A 86m wide by 162m long single floor building was needed to locate an arrangement of twenty-four 1 MA units each comprising four groups of ABB 250 KA power supplies.
A high cost penalty results unless more compact low-voltage / high-current power supply technology can be developed such as a homopolar generator.

## Slide 14
High Temperature Superconductor (HTS) ST Pilot Plant design was developed*
* Developed under a contract with Tokamak Energy (UK)
1.8 aspect ratio, 1.4m R0, 3.2T B0
Pfusion ~ 100MW, QDT ~ 10
PF coils configured for a Super-X/snowflake divertor
negative neutral beam injection for heating and current drive
A 2.35m HTS-ST device has been developed with 0.5m of inboard shield.
To expand ST DEMO operations and evaluate possible FNSF feasibility, high temperature S/C options are being investigated

## Slide 15
CONCLUSIONS
Significant progress was made within the ST-FNSF study these past few years to develop physics, engineering and neutronics details to enhance the selection process of an FNSF program.
Two ST-FNSF designs developed support ex-vessel PF coils to form a Super-X/snowflake divertor that operate with low heat loads, a credible vertical maintenance scheme and an internal arrangement of blanket modules that provide proper port cut-outs to support NNBI yet leave sufficient blanket material to generate high TBR values.
The study found that for a copper TF device, 1.7m was the threshold major radius to operate with a TBR ~ 1and that a device sized at 1m could provide sufficiently high tritium breeding with lower capital and operating cost.

## Slide 16
CONCLUSIONS (cont.)
The 1.7m device size and power supply details make it less favorable when compared to other potential FNSF options; the 1m design appears to be a more cost attractive approach that should be further evaluated.
The HTS ST design was found to have merit in defining a feasible ST power plant and should be pursued to see if it fits within the expectations of an FNSF mission.

## Slide 17
BACK UP SLIDES

## Slide 18
PPPL 4.0-m
AT Pilot Plant
Qengr ≥ 1, TBR > 1
< Wn > 1.7-2.2 MW/m2
Qengr<1, TBR ~ 1
< Wn > ~1 MW/m2
Cu ST-FNSF 1.7-m
Super-X device
Design option size comparisons for pilot plant size device – cu vs. S/C
Qengr <1, TBR < 1
< Wn > ~1 MW/m2
Cu ST-FNSF 1.0-m
Super-X device

## Slide 19
PPPL 4.0-m
AT Pilot Plant
Qengr ~1, TBR < 1
< Wn > ~1 MW/m2
Qengr ≥ 1, TBR > 1
< Wn > 1.7-2.2 MW/m2
TE 1.4-m
HTS ST-FNSF Super-X device
PPPL 2.35-m
HTS ST-FNSF
Super-X design
Qengr ≥ 1, TBR > 1
360 MW fusion power
Design option size comparisons for pilot plant size with S/C magnets

## Slide 20
PPPL 4.0-m
AT Pilot Plant
Qengr ≥ 1, TBR > 1
< Wn > 1.7-2.2 MW/m2
510-647 MW fusion power
K-DEMO 6.8-m device
Pelec ~ 200-600 MW, TBR > 1
< Wn > 2.09 MW/m2
On the road to Demo - size comparisons with S/C magnets
PPPL 2.35-m
HTS ST-FNSF design
Qengr ≥ 1, TBR > 1
360 MW fusion power