## Slide 1: Studies of Next-Step Spherical Tokamaks Using High-Temperature Superconductors
Jonathan Menard (PPPL)
22nd Topical Meeting on the Technology of Fusion Energy (TOFE)
Philadelphia, PA
August 22-25, 2016

## Slide 2: PPPL leading multi-institutional collaborative effort exploring low aspect ratio tokamak concepts
Paper summarizing 5 year study of Cu and HTS STs recently published in Nuclear Fusion

## Slide 3: Possible missions for next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak - DTT
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe
This talk will discuss PPPL-led studies of how low-A “spherical” tokamaks could fulfill these missions

## Slide 4: What is optimal A for HTS FNSF / Pilot Plant?
Pfus / V ~ e(bN k BT )4 at fixed bootstrap fraction
bN and k increase at lower aspect ratio
BT decreases at lower A – depends strongly on:
  Inboard shielding, HTS allowable field and current density
Approach:
Fix plasma major radius and heating power (50MW)
  R0 = 3m – smallest size for Qeng > 1 and high fluence
Apply magnet & plasma constraints (see backup)
  HTS strain: 0.3%, bN: n=1 no-wall, k: 0.95×limit, fGW = 0.8
Vary aspect ratio from A = 1.6 to 4
Vary HTS current density, peak field
  Also scan inboard shielding thickness
Compute QDT, Qeng, and required H98 (unconstrained)

## Slide 5: HTS cables using REBCO tapes achieving high winding pack current density at high BT
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable
Base cable: 50 tapes YBCO Tapes with 38 mm substrate (Van Der Laan, HTS4Fusion, 2015)
Higher Jcable HTS cable concepts under development:
Base Conductor
He Gas Cooled
8kA,
JWP ~ 160MA/m2
7 mm
SS conductor jacket for strength
7 mm
Copper
Conductor on Round Core Cables (CORC)
JWP ~ 70MA/m2 19T

## Slide 6: High TF winding-pack current density required to access highest BT at lower A
12T: ITER-like TF coil limit
(Nb3Sn, 11.8T)
19T: Present CORC HTS limit
JWP [MA/m2]
Chart: Max BT at TF coil [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 18.3214 | 18.7622 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
80 | 16.433 | 17.1602 | 17.7576 | 18.1294 | 18.4409 | 18.7044 | 18.9935 | 18.9996 | 18.9999 | 19 | 19 | 19
40 | 11.266 | 13.8912 | 16.0357 | 16.4935 | 16.8683 | 17.1797 | 17.6277 | 18.277 | 18.8214 | 19 | 19 | 19
30 | 8.4495 | 10.4184 | 12.1777 | 13.3057 | 14.277 | 15.1135 | 16.3799 | 17.2829 | 17.8659 | 18.3192 | 18.9755 | 19
20 | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12.2231 | 13.3857 | 14.3299 | 15.7496 | 16.7393
20 (12T) | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12 | 12 | 12 | 12 | 12
Chart: BT at geometric center [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 2.1314 | 2.8724 | 3.5298 | 3.927 | 4.2687 | 4.5627 | 5.0076 | 5.6937 | 6.3054 | 6.802 | 7.5484 | 8.0687
70 | 1.9117 | 2.6272 | 3.299 | 3.7471 | 4.1431 | 4.4917 | 5.0059 | 5.6935 | 6.3054 | 6.802 | 7.5484 | 8.0687
40 | 1.3106 | 2.1267 | 2.9791 | 3.4089 | 3.7897 | 4.1256 | 4.6459 | 5.477 | 6.2462 | 6.802 | 7.5484 | 8.0687
30 | 0.98296 | 1.595 | 2.2623 | 2.7501 | 3.2076 | 3.6294 | 4.317 | 5.1791 | 5.929 | 6.5583 | 7.5387 | 8.0687
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.6629 | 4.4422 | 5.1301 | 6.2571 | 7.1086
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.596 | 3.9824 | 4.296 | 4.7674 | 5.096
Coil structure sized to maintain ≤ 0.3% strain on winding pack for all cases shown here
Effective inboard WC neutron shield thickness = 60cm

## Slide 7: High current density HTS cable motivates consideration of low-A tokamak pilot plants
ITER-like TF constraints:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW
  Pnet < -90MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
  Small Pnet at A=2.2-3.5
JWP ≥ 70MA/m2,Bmax ≤ 19T
  Pfusion ~500-600MW
  Pnet = 80-100MW at A=1.9-2.3
Chart: Pfusion [MW]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | 246.0028 | 432.7379 | 583.3162 | 607.5533 | 606.7621 | 589.7419 | 571.4392 | 537.6294 | 500.4852 | 453.345 | 358.4489 | 278.381
0.4 | 174.8919 | 332.4576 | 482.5278 | 533.6621 | 558.8914 | 564.7819 | 570.7858 | 537.5829 | 500.4765 | 453.3423 | 358.4484 | 278.3808
0.5 | 51.1869 | 172.9943 | 358.5903 | 407.2527 | 434.1847 | 444.1135 | 462.48 | 481.3769 | 487.0152 | 453.345 | 358.4489 | 278.381
0.6 | 19.8048 | 68.1159 | 153.2279 | 212.6847 | 264.1296 | 304.1657 | 373.389 | 409.141 | 418.1467 | 406.719 | 357.0235 | 278.381
0.7 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 139.6142 | 171.0165 | 189.3741 | 197.5059 | 184.0685
20 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 131.5217 | 119.8912 | 105.974 | 79.8077 | 59.401
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
JWP [MA/m2]
A ~ 2 attractive at high JWP
(12T)

## Slide 8: A ≥ 2 pilot plant scenarios have elevated H > 1, fBS ~ 80%, IP = 6-12MA
JWP [MA/m2]
Effective inboard WC neutron shield thickness = 60cm

## Slide 9: A ≤ 2 maximizes TF magnet utilization
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
JWP = 70MA/m2

## Slide 10: Need inboard breeding for TBR > 1 at A=2
10cm IB shield sufficient for TBR > 1.04
Outboard TBR ~ 0.92
TBR
Required TBR = 1.04
(4% margin)

## Slide 11: Breeding blanket thickness model

## Slide 12: A ≥ 3 maximizes blanket utilization
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
JWP = 70MA/m2

## Slide 13
A=2, R0 = 3m HTS-TF FNSF / Pilot Plant
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%
H98 = 1.8, HPetty-08 = 1.3
fgw = 0.80, fBS = 0.76
Startup IP (OH) ~ 2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW, ENBI = 0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence = 7 MWy/m2
Cryostat volume ~ 1/3 of ITER

## Slide 14: Inboard and outboard blanket vertical maintenance
Outboard blanket removed
Inboard blanket removed once outboard blanket sectors removed – depending on the toroidal extent of the inboard blanket

## Slide 15: Long-leg divertor Pdiv = 9MW/m2, Rstrike = 4.2m
Long-leg / Super-X
Shorter leg LM divertor
Geometry also compatible with
“vapor box” concepts (Ono / Goldston)
Liquid metal (short-leg) Pdiv = 21MW/m2, Rstrike = 2.5m

## Slide 16: Exploring liquid metal divertor design similar to flowing water curtain systems
Ferritic steel backing plate
Shield block
LM containment structure
LM injector system can be assembled in a single or double unit

## Slide 17: HTS ST-FNSF design with Li flow on divertor and inboard surfaces
Double null liquid metal divertor system
Li flows from upper divertor down the inboard wall, exiting just after the lower inboard divertor.
Separate Li cooling of lower divertor

## Slide 18: Benefits of shorter-leg LM high-heat-flux divertor:
Significantly reduce outboard PF coil current
  Reduced PF size, force, structure
Eliminate separate upper cryo-stat (for PF5U)
1
2
3
4
5
6
7
8
Li wall pumping could help increase H

## Slide 19: Summary
Developed new self-consistent configurations for low-A FNSFs / Pilot Plants
  Long-leg and/or LM divertor, T self-sufficient, only ex-vessel TF and PF coils, vertical maintenance
Compact Pilot Plants achievable by combining improved stability of low-A + advanced magnets
  Optimal A will be informed by results from NSTX-U and MAST-U and REBCO TF magnet development
Liquid metal divertors for high heat flux could simplify cryostat, reduce coil currents/forces
  Higher confinement from liquid Li also beneficial

## Slide 20
Backup slides

## Slide 21: Detailed breeding calculations completed for A=2
Step 1- Infinite media of LiPb
Step 2- LiPb confined to OB FW/blanket
Step 3- Assembly gaps added
Step 4- Homogeneous mixture of blanket in upper and lower ends of OB blanket
Step 5- FW material added
Step 6- Side, back, and front walls added
Step 7- Cooling channels added
Step 8- SiC FCI added
Step 9- Stabilizing shells added
Step 10- MTM only inserted (TBR relative to Step #9)
Step 11- 4 TBMs only inserted (TBR relative to Step #9)
Step 12- 4 NBIs only inserted (TBR relative to Step #9)
Step 13- all MTM, 4 TBMs, and 4 NBIs inserted
Step 14 – include inboard breeding blanket

## Slide 22: Comparison of low-A FNSF / Pilot Plants

## Slide 23: Plasma constraints
Fix plasma major radius at R0 = 3m
  Chosen to be large enough to allow space for HTS neutron shield and access Qeng > 1 for range of A
Inboard plasma / FW gap = 4cm
Use e-dependent k(e), bN (e) (see next slide)
Greenwald fraction = 0.8
q* not constrained
  q* is better e-invariant than q95 for current limit
  Want to operate with q* > 3 to reduce disruptivity
0.5 MeV NNBI for heating/CD – fixed PNBI = 50MW
H98y2 adjusted to achieve full non-inductive CD

## Slide 24: Aspect ratio dependence of limits: k(e), bN(e)
NSTX data at low-A
  Also NSTX-U/ST-FNSF modelling
DIII-D, ARIES-AT for higher A
  k  1.9 for A  
Profile-optimized no-wall stability limit at fBS ≈ 50%
  Menard PoP 2004
bN  3.1 for A  
bT  A-1/2 (1+k2) bN2 / fBS
 Pfus  e [k(e) bN(e) BT(e)]4
e = A-1
Pilot study uses 0.95×k value shown here:

## Slide 25: Engineering constraints
Magnet constraints
  Maximum stress in TF magnet structure = 0.66 GPa
  HTS tape/cable strain limit 0.3% (equivalent to 0.4 GPa)
  Winding pack current density (CORC 2015) 70 MA/m2
  OH at small R  higher solenoid flux swing for higher A
Shielding / blankets
  HTS fluence limit: 3.5-5 x 1022 n/m2
  Shield:10x n-shielding factor per 15-16cm WC for HTS TF
  Include inboard & outboard breeder thickness for TBR ~ 1
    “Effective shield thickness” includes shield + DCLL blanket
Electrical system efficiency assumptions:
  30% wall plug efficiency for H&CD - typical of NNBI
  ≥ 45% thermal conversion efficiency - typical of DCLL
    Also include pumping, controls, other sub-systems
    See Pilot Plant NF 2011 paper for more details

## Slide 26: Simplified TF magnet design equations
From J. Schwartz, Journal of Fusion Energy, Vol. 11, No. 1, 1992

## Slide 27
A=2, R0 = 3m device TF inboard leg showing
allocated space for case and winding
0.167 m2 winding area
Current per coil: 6 MA
Winding Cd: 35.9 MA/m2

## Slide 28
CORC Conductor – Achieved now
10 mm
10 mm
6 mm
857 turns @ 7 kA
(848 turns shown; a few additional turns required)
Base Conductor – Helium Gas Cooled
7 mm
SS conductor jacket for strength
7 mm
Copper
750 turns @ 8 kA
(750 turns shown)

## Slide 29: HTS performance vs. field and fast neutron fluence

## Slide 30: Neutronics analysis for HTS TF shielding

## Slide 31: HTS TF lifetime is very strong function of inboard shielding thickness
Inboard shield + blanket equivalent to 60cm WC 
3FPY  6-7MWy/m2  fulfill FNSF requirement

## Slide 32: 3-D Neutronics Model
Simple CAD Model outlining components (from T. Brown):
  10 cm IB modules
  20 cm OB modules
R-Z neutron source
IB shield and VV optimization and composition by UW.
OB blanket internals and composition by UW
Detailed CAD of blanket by UW
UW DAGMC code couples CAD to 3D MCNP neutronics code.

## Slide 33: CAD Geometry of OB Blanket with Ports
Detailed Blanket Internals
Stabilizing
Shells
MTM
TBM
4 NBIs

## Slide 34: Local details of Li divertor / inboard FW
Lower divertor
Inboard DCLL blanket
Inboard shield
Li and inboard component piping
Li drain plenum
Upper Li feed
Li flow on girdle shell

## Slide 35: Lower Li containment system
One of ten 100 mm ID Li inboard drain lines
Li flows over inboard surface to a continuous trough that feeds ten Li drain lines.
Base Li return trough

## Slide 36: Inboard FW / DCLL / shield components
300 mm WC inboard shield
200 mm DCLL blanket system
10 mm Li surface metal structure (girdle)
As a first pass design it is assumed that these components will be electrically continuous
…analysis will follow.

## Slide 37
Assessing long-leg / deep-V slot divertor
PF coils outside TF
Increase strike-point radius ~2× to reduce q|| and peak heat flux
Divertor PFCs in region of reduced neutron flux
Narrow divertor aperture for increased TBR
More space for breeding at top/bottom of device

## Slide 38: Long-leg / Super-X aids heat flux reduction
A=2 HTS TF FNSF/Pilot
lq ~ 1mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment likely reduces peak q by further factor of 2-4