## Slide 1
TRANSP Modeling of Fast-ion D (FIDA) Signals
Bill Heidbrink, Nathan Bolte, Cami Collins, Deyong Liu, Guangzhou Hao, Luke Stagner
Beam modulation experiments with active FIDA and NPA signals
Passive FIDA Signals

## Slide 2
FIDA is an application of Charge Exchange Recombination Spectroscopy
The fast ion exchanges an electron with a neutral
Neutrals in the n=3 state relax to an equilibrium population; some radiate
The Doppler shift of the emitted photon depends on a component of the fast-ion velocity
3 cm
Heidbrink, RSI 81 (2010) 10D727

## Slide 3
Active FIDA measurements use an injected neutral beam
Reactions with edge neutrals produce passive FIDA light

## Slide 4
FIDASIM is a synthetic diagnostic code
Heidbrink, Comm. Comp. Phys. 10 (2011) 716
A calculated fast-ion distribution function is input to the code—often use “dumped” TRANSP NUBEAM distributions
Computes four neutral populations: Full, half, & third energies from injected beam + halo
Solves energy-level resolved time-dependent collisional-radiative equations
Doppler shift and Stark splitting of radiated photons

## Slide 5: Experiment compares modulated fast-ion signals to “classical” TRANSP predictions
Modulated Neutrons
Collins NF 57 (2017) submitted
Transport by Alfven eigenmodes causes differences between measured & calculated signals

## Slide 6: Conditionally average signals & predictions for FIDA & neutral particle analyzer (NPA) signals
Heidbrink, NF 56 (2016) 112011
TRANSP Workflow
Special run with only the modulated beam & 106 markers (good MC statistics)
Dump distribution function every 2.5 ms for 6 beam cycles (~ 120 times)
Run FIDASIM for each timeslice
Conditionally average FIDASIM output
2.4 MW
Solid = Data
Dashed = TRANSP

## Slide 7
A dedicated study of passive FIDA light was performed on DIII-D
The active beams were always off  no active signal
Other beams were modulated to produce fast ions
Bolte, NF 56 (2016) 112023
Conditionally average the signals on either the beam modulation or the sawteeth

## Slide 8
“Light-ion beam probe” technique: arrange conditions so orbit passes close to a loss detector  measure displacement of orbit by instabilities
Plan view of DIII-D
Xi Chen, Phys. Rev. Lett. 110 (2013) 065004
Three distinct fast-ion populations produce the measured signals: First orbit
FIDA
Orbits that traverse edge produce passive FIDA light
TRANSP does not compute this fast-ion population

## Slide 9
Three distinct fast-ion populations produce the measured signals: Edge axisymmetric
Bolte, NF 56 (2016) 112023
Conditionally averaged modulated distribution function (with average subtracted)

## Slide 10
Three distinct fast-ion populations produce the measured signals: Expelled by sawtooth
Bolte, NF 56 (2016) 112023
Core fast-ion population prior to sawtooth
Use TRANSP sawtooth model to predict # that are expelled
Estimate expected signal using core distribution function

## Slide 11
Use TRANSP cold neutrals to estimate passive FIDA signal
Analysis Workflow
Dump distribution function every few ms
Extract 1D neutral profile from TRANSP output
Insert as a cold neutral population into FIDASIM
Conditionally average FIDASIM output
Bolte, NF 56 (2016) 112023

## Slide 12: Passive signals are relatively large on NSTX-U
Plan view of FIDA geometry
Elevation view of FIDA geometry
V-FIDA passive
V-FIDA active
T-FIDA passive
T-FIDA active
NSTX-U#205080
Active views of Beamline #1
Large orbit & gyroradius  many ions traverse cold-neutral region

## Slide 13: Injected and Edge Neutrals Produce FIDA Signals
Use “passive FIDA” workflow developed for DIII-D
T-FIDA: the active and passive signals are comparable in magnitude.
For geometrical reasons, the passive contribution is smaller on V-FIDA
Note: Not all chords agree this well

## Slide 14
Conclusions & Outlook
TRANSP-based workflow works well for modeling active FIDA & NPA data in modulation experiments
Passive signals can be significant
A better neutral density model within TRANSP is desirable
FIDASIM will be modified to include cold neutrals as a standard neutral species

## Slide 15
Desired TRANSP Upgrades
2D “cold” neutral density model (? & ?)
Beam deposition outside the Last Closed Flux Surface (Gorelenkova & Van Zeeland)
Fast-ion distribution function in constants-of-motion coordinates, including smooth derivatives (Breslau & Liu)